## Slide 1
VLSI DESIGN
Dr. Vijay Rao Kumbhare
Assistant Professor (ECE)
K L University, Hyderabad
23EC2211A

## Slide 2: Contents
MOSFET BASICS:-
MODES; MOSFET as switch;
Symbols; VI Characteristics
Previous Lecture
Course introduction with Pre-requisite
Course handout and evaluation pattern
CH, Evaluation Plan, Formative Assessment

## Slide 3: Course Introduction and Objective
The purpose of this course is to develop a strong foundation and skills in analysis and design of low power VLSI circuit.
Understand the fundamentals of VLSI circuit design, including device physics, transistor models, and circuit analysis techniques (CO-01)
Gain proficiency in CMOS layout design rules leading to successful fabrication of VLSI circuits. (CO-02)
Acquire hands on experience in different industry level VLSI CAD tools like CADENCE through successful back annotation of VLSI circuits. (CO-03)
Develop skills in optimization techniques including layouts, area reduction through transistors reduction and performance (delay and power) enhancement. (CO-04)
Explore advanced topics in full custom VLSI techniques like static and dynamic memory design. (CO-05)
Course Rationale :

## Slide 4: Course Content: VLSI DESIGN (22EC2211A)
L-T-P-S | 4-0-4-2 | Credit | 6.5
Pre-requisites | NIL | Contact Hours | -
MOS Transistor Theory: Introduction to the metal oxide semiconductor (MOS) structure, Long-channel I-V characteristics, C-V characteristics, non-linear I-V effects, and DC transfer characteristics. CMOS Process Technology: Fabrication process flow- basic steps, the CMOS n-Well process, layout design rules, stick diagram, full-custom mask layout design.
Circuit Characterization and Performance Estimation: : Introduction, Delay Estimation, Logical effort and transistor sizing, power dissipation, interconnect, design margin, reliability, scaling. MOS Inverters: Resistive load, depletion load, enhancement load, CMOS inverter, Static and Dynamic characteristics.
Combinational CMOS Logic Circuits: MOS logic circuits with depletion nMOS loads, MOS Inverter - Static Characteristics, Switching Characteristics, and Interconnects effects, CMOS logic circuits, complex logic circuits, CMOS transmission gates (pass gates), ratioed, dynamic and pass transistor logic circuits.
Sequential MOS logic circuits: Behavior of bi-stable elements, SR latch circuits, clocked latch and flip-flop circuits, CMOS D-latch, and edge-triggered flip-flop. Timing path, Setup time and hold time static, an example of setup and hold time static, setup and hold slack, clock skew and jitter, Clock, reset, and power distributions. Memory Design, SRAM, DRAM structure, and implementations.
Syllabus

## Slide 5: Text and Reference Books
N. H. E. Weste, and C. Harris, Principles of CMOS VLSI Design: A System Perspective, 3rd Edition, Pearson Education, 2007
Kang, Sung Mo, and Yusuf Leblebici, CMOS digital integrated circuits, Second edition, MacGraw-Hill, 2003
Debaprasad Das, VLSI Design, OXFORD Higher Education.Jacob Baker, “CMOS Mixed Signal Circuit Design”, John Wiley, (2008)
Jan M. Rabaey, “Digital Integrated Circuits” Pearson Education, 2003
Douglas A. Pucknell, and Kamran Eshraghian - Basic VLSI design, Prentice-Hall, 1994.
J. Rabaey, A. Chandrakasan, and B. Nikolic, Digital Integrated Circuits: A Design Perspective, 2nd Edition, Prentice Hall, 2004.
Reference Books
Text Books

## Slide 6: EVALUATION PLAN

## Slide 7: MOSFET Basics
Any voltage-controlled current source can provide signal amplification.
MOSFETs also behave as controlled sources but their characteristics are different from those of bipolar transistors.
A simple geometry consisting of a conductive (e.g., metal) plate, an insulator (“dielectric”), and a doped piece of silicon.
Such a structure operates as a capacitor
Figure 1 (a) Hypothetical semiconductor device, (b) operation as a capacitor, (c) current flow as a result of potential difference.

## Slide 8
Vg < 0
When a negative voltage is applied to the gate
Accumulation
MOSFET Capacitor

## Slide 9
Vg > 0
Depletion
When a small positive voltage is applied to the gate
Depletion
MOSFET Capacitor

## Slide 10
0 > Vg > Vth
Inversion
When a positive voltage above threshold voltage is applied to the gate
Channel
MOSFET Capacitor

## Slide 11: MOSFET
Flow of charge from “Source” to “Drain” is controlled by the “Gate” voltage.
Control by the Gate voltage is achieved by modulating the conductivity of the semiconductor region just below the gate. This region is known as the channel
Metal Oxide Semiconductor Field Effect Transistor
Four terminal device: Source (S), Gate (G), Drain (D), and Body (B).
Fig. 1 Basic Structure of MOSFET

## Slide 12: Mode of Operation
Depletion mode and enhancement mode.
The formation of a channel between the source and drain can act as N-type or P-type MOSFET depending on the carriers doped in the channel region.
Depletion mode: The transistor requires the Gate-Source voltage (VGS) to switch the device “OFF”. The depletion-mode MOSFET is equivalent to a “Normally Closed” switch.
Enhancement Type: The transistor requires a Gate-Source voltage (VGS) to switch the device “ON”. The enhancement-mode MOSFET is equivalent to a “Normally Open” switch.

## Slide 13: N-channel vs. P-channel
For current to flow, VGS > VT
  to form n-type channel at surface
NMOS
PMOS
p-type Si
N+ poly-Si
N+
N+
n-type Si
P+ poly-Si
P+
P+
For current to flow, VGS < VT
  to form p-type channel at surface
Note: VT denotes the threshold voltage, some textbook uses the Vt notation.
Enhancement mode: VT > 0
Enhancement mode: VT < 0
Depletion mode: VT < 0
  Transistor is ON when VG=0V
  Transistor is OFF during - VG
Depletion mode: VT > 0
  Transistor is ON when -VG
  Transistor is OFF during +VG

## Slide 14
Devices | Operating State | Applied Voltage as Gate terminal for | 
 |  | N- channel | P-channel
Depletion type | ON | – VG Turns OFF | +VG Turn OFF
Enhancement type | OFF | + VG Turns ON | – VG Turn ON
Table 1 Types of MOSFET having N-type and P-type channel
Fig. 2 Symbolic representation of n-channel/p-channel MOSFET under (a) depletion condition and (b) enhancement condition.
(a)
(b)

## Slide 15: N-channel Enhancement type MOSFET
Perspective View
Cross-sectional View
Fig. 3 Physical structure of n-channel enhancement MOSFET (a) perspective view and (b) cross-sectional view.

## Slide 16: N-channel Enhancement type MOSFET
The gate electrode is placed on top of a very thin insulating oxide (SiO2) layer.
Fig. 3 Cross-sectional view of n-channel enhancement MOSFET
There are a pair of small n-type regions just under the drain and source electrodes.
If apply a +Ve voltage to gate (G), will push away the “holes” inside the p-type substrate and attracts the moveable electrons in the n-type regions under the source and drain electrodes.
Increasing the +Ve voltage of gate (G) pushes the p-type holes further away and enlarge the thickness of the created channel.
As a result, source to drain current increases-this is why this kind of transistor is called as enhancement mode device.

## Slide 17: P-channel MOSFET
These behave in a similar way, but they pass the current when a –Ve gate voltage creates an effective p-type channel layer under the insulator.
Fig. 4 Cross-sectional view of p-channel enhancement MOSFET
All the voltage and current sign are reversed as compared to N-channel MOSFET.
The free charges that moves from end to end are positively charged (holes).
The PMOS and NMOS transistor are said to be complementary devices.

## Slide 18: Operation of N-channel enhancement MOSFET
For an n-channel device with its source and substrate grounded (i. e., VS=VB=0 V).
For any value of VDS: (Operation with zero gate voltage)
when VGS <0 (accumulation), the source to drain path consists of two back to back diodes.
One of these diodes is always reverse biased regardless of the drain voltage polarity.
when 0<VGS <VT (depletion), there is a deficit of electrons and holes making the channel highly resistive.
No Drain current can flow.
VDS ≥ 0 V
Fig. 5 n-channel enhancement MOSFET at zero gate voltage.

## Slide 19
Consider now the Inversion case:
First, VDS = 0:
when VGS > VT , an induced n- type region, an “inversion layer”, forms in the channel and “electrically connects” the source and drain
The channel is created by inverting the substrate surface from p-type to n type. Hence the induced channel is also called an inversion layer.
The value at which a sufficient number of mobile electrons accumulate in the channel region to form a conducting channel is called the threshold voltage (VT).
VT ranges from 0.3 to 1V.
Fig. 6 n-channel enhancement MOSFET at positive gate voltage.

## Slide 20
Inversion case, VGS > VT (continued): (Applying a small VDS)
When VDS >0 , the induced n-type region allows current to flow between the source and drain.
Fig. 8 Drain current (ID) verses drain voltage (VD) when in the linear or “triode”* region.
Fig. 7 n-channel enhancement MOSFET with VGS>VT and a small VDS applied
The induced channel acts like a simple resistor. Thus, this current, ID, depends linearly on the Drain voltage VD. This mode of operation is called the linear or “triode”* region.

## Slide 21
Inversion case, VGS > VT (continued):
When VDS increases a few tenths of a volt (>0):
Fig. 9 n-channel enhancement MOSFET with VGS>VT and increased VDS .
The depletion region near the drain widens (N+ drain is positively biased – i.e. reverse biased with respect to the substrate).
The electron concentration in the inversion layer near the drain decreases as they are “sucked out” by the drain voltage.
Channel conductance decreases resulting in a drop in the slope of the ID – VD curve.
Fig. 10 Drain current verses drain voltage for increasing VDS (still in the “linear” or triode region).

## Slide 22
Inversion case, VGS > VT (continued):
The inversion layer eventually vanishes near the drain end of the channel. This is called “Pinch-Off” and results in a Flat ID-VDS curve.
The drain-source voltage, VDS, at which this occurs is called the saturation voltage, Vsat while the current is called the saturation current, IDsat.
Fig. 11 The drain current versus the drain-to source voltage for an enhancement type NMOS transistor operated with VGS=VT+VOV.
Where VT and VOV denote threshold voltage and over drive voltage, respectively.

## Slide 23
Inversion case, VGS > VT (continued):
For VDS>Vsat the channel length, L, effectively changes by a value ΔL.
The region of the channel, ΔL is depleted and thus, is high resistivity.
If ΔL ~L, the voltage dropped across the channel (Vsat) varies greatly with VDS due to large modulations in the electric field across the pinched off region ( E=[VDS -Vsat]/[ΔL]).
In this case, ID increases slightly with VDS.
If ΔL <<L, the voltage at the end of the channel will be constant (Vsat ) for all VDS>Vsat.
  ID will be constant.

## Slide 24
Finally,
ID-VDS curves for various VGS:
Fig. 12 The Final drain current versus the drain-to source voltage for an enhancement type NMOS transistor.

## Slide 25: The Depletion type MOSFET
Its structure is similar to that of the enhancement-type MOSFET with one important difference:
The negative VGS is said to deplete the channel of its charge carriers, and this mode of operation (negative VGS) is called depletion mode.
The depletion MOSFET has a physically implanted channel.
An n-channel depletion-type MOSFET has an n-type channel region connecting the n+ source and the n+ drain regions at the top of the p-type substrate.
If a voltage VDS is applied between drain and source, a current ID flows for VGS = 0.
There is no need to induce a channel, unlike the case of the enhancement MOSFET.

## Slide 26: Enhancement Mode verses Depletion Mode MOSFET
N-channel MOSFET
Enhancement mode
Depletion mode
Structure
Symbol

## Slide 27: Derivation of I-V Characteristics
1. Channel Charge Density
From Qch = CV
C is the gate capacitance per unit length and V the voltage difference between the gate and the channel, then Qch is the desired charge density.
C = WCox
V = VGS − VTH because no mobile charge exists for VGS < VTH.
Qch = WCox(VGS − VTH).
Qch is expressed in coulomb/meter.
2. Drain Current at the linear, or triode, region.
Consider a bar of semiconductor having a uniform charge density (per unit length) equal to Qch and carrying a current I

## Slide 28: Derivation of I-V Characteristics
2. Drain Current at the linear, or triode, region. (as long as VDS kept in low level i.e VDS < VGS ‐ VTH)
Drift time, td, is directly proportional to the channel length L, and inversely proportional to the drift velocity of electrons, vd
Drift velocity, vd, is proportional to the horizontal electric field, εy, i.e.:
where µn is the electron mobility in the channel. The value of the horizontal electric field, εy, is, approximately, calculated as follows:
the following expression for IDS can be written as:
where kn is called conductivity factor for NMOS transistors. It is given by:

## Slide 29: Derivation of I-V Characteristics
The NMOS transistor operates in the linear, or triode, region, as long as VDS kept in low level i.e VDS < VGS ‐ VTH
Fig. 1 IDS ‐VDS curves of the NMOS transistor in linear region with VGS as parameter.
IDS is proportional to VDS.
Practically, in linear region, the NMOS transistor acts like a variable resistance, Ron, whose value depends on Vov. Ron is calculated as follows:
2. Drain Current at the linear, or triode, region. (as long as VDS kept in low level i.e VDS < VGS ‐ VTH)
(A)
(B)

## Slide 30: Derivation of I-V Characteristics
3. Drain Current at the linear, or triode, region. (As VDS is increased, the charge channel narrows at the drain end)
VDS modifies the voltage, and, the charge along the channel.
The voltage component due to VDS is maximum at the drain end, while it is zero at the Source end.
Suppose a linear distribution of the voltage component due to VDS along the channel, its average value can be approximately estimated to be VDS/2.
Then, a more accurate calculation of the channel charge can be obtained by adding VDS/2 in the charge expression
A more accurate calculation of the IDS current in linear region is also possible:
Drain Current at the linear, or triode, region.
(C)
(D)

## Slide 31: Derivation of I-V Characteristics
4. Drain Current at Saturation Region (As VDS approaches VGS‐VTH, )
As VDS approaches VGS‐VTH, the channel charge approaches zero at the Drain end.
When VDS compensates for the overdrive voltage VGS‐VTH, VGD results to be equal to the threshold voltage VTH
In this bias condition, no channel charge is available at the Drain end. The conducting channel pinches‐ off, disconnecting the Drain.
The VDS value that produces the channel pinch‐off is called saturation voltage (VDS,sat).
(E)
(F)
Substituting the VDS value in equation A, the expression of the IDS at the pinch‐off is obtained:
For your reference, Eq. A
Therefore, when VDS increases, this depletion region enlarges, and the pinch‐off point moves toward the Source.

## Slide 32: Current-voltage characteristics
The characteristics can be measured at dc or at low frequencies and thus are called static characteristics.
where k’n , gDS , and rDS are process transconductance parameter, channel conductance, and linear resistance, respectively.
The dynamic effects that limit the operation of the MOSFET at high frequencies and high switching speeds.

## Slide 33
Fig. 13 The drain current versus the drain-to source voltage for an enhancement type NMOS transistor.

## Slide 35: Second Order Effects:
Following are the list of second order effects of MOSFET.
Channel length modulation
Velocity Saturation
Mobility Degradation
Threshold voltage – Body effect
Subthreshold region
Drain Punchthrough
Impact Ionization – Hot Electrons

## Slide 36: Channel Length Modulation
Thus, when a high impedance current source is required, longer channel transistors are used.
This reduces the length of the channel which impacts current. The model current equation must be modified to
The length of the channel changes with changing values of VDS.
As the value of VDS is increased, it causes the depletion region of the Drain junction to grow.
In general, lambda is proportional to channel length.
The effects of channel length modulation become more pronounced for smaller feature sizes.

## Slide 37: Channel Length Modulation
This phenomenon yields a larger drain current as VDS increases because ID ∝ 1/L1

## Slide 38: Velocity Saturation
Carrier velocity increases with increasing electric fields.
However, once the critical lateral electric field is reached, the velocity of the carriers does not increase any further.
The current does not increase at the expected rate. Rather, the current increases very little.
At high electric fields (VDS), carrier mobility degrades, eventually leading to a constant velocity.
This is caused by an increased rate of collision and carrier scattering.
Owing to their very short channels (e.g., 0.1 μm), modern MOS devices experience velocity saturation even with drain-source voltages as low as 1 V.
V= μE

## Slide 39: Mobility Degradation
With increasing VGS, vertical electric fields increase.
This increase causes a rise in the number of carrier collisions, which degrades carrier mobility.
The current flowing through the transistor is expected by the ideal models.
Mobility decreases with increasing temperature.

## Slide 40: Body Effect
In MOSFETs, we have assumed that both the source and the substrate (also called the “bulk” or the “body”) are tied to ground.
However, this condition need not hold in all circuits.
An interesting phenomenon occurs as the source-substrate potential difference departs from zero:
The threshold voltage of the device changes.
In particular, as the source becomes more positive with respect to the substrate, VTH increases. Called “body effect,”
If the source terminal rises to a positive voltage while the substrate is at zero, then the source-substrate junction remains reverse-biased and the device still operates properly.

## Slide 41: MOSFET Device Models
Small Signal Model Analysis
In the small-signal model, there is an output resistance r0 and the current source is gmVgs,
so if we can find the Transconductance (gm), we can find the value of current in this circuit.
Output resistance r0 is the fluctuation of drain-source voltage to current.

## Slide 42: MOSFET Device Models

## Slide 43: MOSFET Transconductance

## Slide 44
Input Resistance
The gate of an MOS transistor is insulated from the channel by the SiO2 dielectric
The low-frequency gate current is essentially zero and the input resistance is essentially infinite.
Output Resistance
where VA is the Early voltage, λ is the channel-length modulation parameter, ID is the drain current without channel-length modulation, and ro is the small-signal output resistance of the transistor.

## Slide 45: Numerical
the intrinsic gain, gmrO , is equal to 20

## Slide 46: MOSFET Device Models
Large Signal Model Analysis

## Slide 47: Contents
Introduction of MOSFET Amplifiers –
  Common Source (CS),
  Common Gate (CG) and
  Common Drain (CD) Amplifiers,
Their brief characteristics, pros and cons

## Slide 48: The MOSFET Amplifier
(a) Common Source (CS)
(b) Common Gate (CG)
(c) Common Drain (CD)
The linear amplifiers are necessary in analog electronic system.
The term small signal means linearization of the ac equivalent circuit.
The linear amplifier means the use of superposition.
The various possible configurations of MOSFET amplifiers is considered
The Three Basic Configurations

## Slide 49: Characterizing Amplifiers
Find gain, input and output resistance
Fig. 1(a) An amplifier fed with a voltage signal vsig having a source resistance Rsig, and feeding a load resistance RL; (b) Equivalent-circuit;
(a)
(b)
An amplifier fed with a signal source having an open-circuit voltage vsig and an internal resistance Rsig.
The input resistance Rin represents the loading effect of the amplifier input on the signal source.
(1)
(2)

## Slide 50
The second parameter is the open-circuit voltage gain Avo
The third parameter is the output resistance Ro,
The controlled source Avovi and the output resistance Ro represent the Thévenin equivalent of the amplifier output circuit, and the output voltage can be expressed as
Thus the voltage gain of the amplifier, Av , can be found as
The overall voltage gain Gv
(3)
(4)
(5)
(6)
(7)
(8)

## Slide 51: The Common-Source (CS) Amplifier
Of the three basic MOS amplifier configurations, the common source is the most widely used.
Characteristic Parameters of the CS Amplifier
Replacing the MOSFET with its hybrid- model, we obtain the CS amplifier equivalent circuit shown in Fig. 2(b).
We shall use this equivalent circuit to determine the characteristic parameters Rin, Avo, and Ro,
(a)
(b)
Fig. 2(a) common source amplifier circuit and (b) MOSFET replaced with its hybrid π-model
(9)

## Slide 52: The Common-Source (CS) Amplifier
The output voltage vo is found by multiplying the current (gmvgs) by the total resistance between the output node and ground,
Since vgs = vi, the open-circuit voltage gain Avo ≡ vo/vi can be obtained as
Observe that the transistor output resistance ro reduces the magnitude of the voltage gain.
RD is usually much lower than ro and the effect of ro on reducing |Avo| is slight. Thus in many case we can neglect ro
(10)
(11)
(12)

## Slide 53: The Common-Source (CS) Amplifier
Overall Voltage Gain:
If a load resistance RL is connected to the output terminal of the amplifier, this resistance will appear in parallel with RD.
This expression together with the fact that , vi = vsig provides the overall voltage gain,
(13)
(14)
Fig. 2(b)

## Slide 54: The Common-Source (CS) Amplifier
The output resistance Ro is the resistance seen looking back into the output terminal with vi set to zero.
From Fig. 2(b) we see that with vi set to zero, will be zero, vgs will be zero, and thus gmvgs will be zero, resulting in
Here, ro has the beneficial effect of reducing the value of Ro. In discrete circuits, this effect is slight and we can make the approximation
(15)
(Fig. 2(b))
(16)

## Slide 55: The Common Gate (CG) Amplifier
From inspection of the equivalent circuit of Fig. 3(b), we see that the input resistance
To determine the voltage gain Avo, we write at the drain node
and substitute for the source current i from
(17)
Fig. 3(a) CG amplifier circuit and (b) MOSFET replaced with its T model
(18)
To obtain
(19)
(20)
(a)
(b)

## Slide 56: The Common Gate (CG) Amplifier
The output resistance of CG
which is the same as in the case of the CS amplifier
The gain of the CG amplifier has the same magnitude as that of the CS amplifier,
The signal transmission factor vi/vsig can be very small and the overall voltage gain Gv can be correspondingly small.
(21)
(22)
(23)
and
Fig. 3(b)

## Slide 57: Common-Drain (CD) Amplifier
The common drain amplifier commonly known as the source follower.
Fig. 4 (a) Common-drain amplifier (b) Equivalent circuit of the source follower obtained by replacing the MOSFET with its T model. Note that ro appears in parallel with RL and in discrete circuits, ro>>RL . Neglecting ro, we obtain the simplified equivalent circuit in (c).

## Slide 58
The characteristics Parameters of the Source Follower
Fig. 4(b)
Since the MOSFET has a resistance RL connected in its source terminal, it is most convenient to use the T model, as shown in Fig. 4(b)
Av can be obtained from the voltage divider formed by 1/gm and RL as
Setting
, we obtain
(24)
(25)
The output resistance Ro is found by setting vi = 0
The overall voltage gain:
(26)
(27)

## Slide 59
Fig. 2
Fig. 3
Fig. 4
Fig. 1(a)

## Slide 60: Properties of CS, CG, and CD amplifier
1. Common source
high input impedance, low output impedance, high gain, BW varies inversely with gain. Common voltage amplifier circuit.
2. Common gate
low input impedance, low output impedance, low gain, high BW, unity current gain. Common current regulator circuit.
3. Common drain (also called source follower)
high input impedance, low output impedance, unity voltage gain, high BW. Common voltage buffer circuit, impedance matching, simple output stage.

## Slide 61: Contents
The CS and CE amplifiers with Current source load
Determination of intrinsic gain,
Effect of output resistance of the current source load

## Slide 62: The CS and CE amplifiers with Current source load
The basic gain cell in an IC amplifier is a common-source (CS) or common-emitter (CE) transistor loaded with a constant-current source.
we have replaced the resistances RD and RC (from CS and CE) with constant-current sources.
Due to difficult in IC technology to implement resistances with reasonably precise values.
It is much easier to use current sources, which are implemented using transistors
Using a constant current source, we are in effect operating the CS and CE amplifiers with a very high load resistance; thus we can obtain a much higher gain.

## Slide 63
Figure 1 The basic gain cells of IC amplifiers: (a) current-source- or active-loaded common-source amplifier; (b) current-source- or active-loaded common-emitter amplifier; (c) small-signal equivalent circuit of (a); and (d) small-signal equivalent circuit of (b).
(a)
(b)
(c)
(d)

## Slide 64
Figure 1 The basic gain cells of IC amplifiers: (a) active-loaded common-source amplifier (b) small-signal equivalent circuit
(b)
Active-loaded common-source amplifier
Small-signal analysis of the current-source-loaded CS amplifier can be performed by utilizing their equivalent-circuit models,
From Fig. 1(b) we obtain for the active-loaded CS amplifier:
Since the current-source load is assumed to be ideal, it is represented in the models by an infinite resistance.
(a)

## Slide 65
Figure 2 The basic gain cells of IC amplifiers: (a) active-loaded common-source amplifier (b) small-signal equivalent circuit
Active-loaded common-emitter amplifier
Small-signal analysis of the current-source-loaded CE amplifier can be performed by utilizing their equivalent-circuit models,
From Fig. 2(b) we obtain for the active-loaded CE amplifier:
(b)
Thus both circuits realize a voltage gain of magnitude gmro. Since this is the maximum gain obtainable in a CS or CE amplifiers.
(a)

## Slide 66
Recall from our study of the MOSFET; there are three possible expressions for gm. Two of these are particularly useful here
For the MOSFET r0 we have
where VA is the Early voltage and V’A is the technology-dependent component of the Early voltage.
and
Utilizing each of the gm expressions together with the expression for , we obtain for A0
, Alternatively
and
(3)
(4)
(5)
(6)

## Slide 67: Numerical

## Slide 69: Assignment

## Slide 70: Effect of the Output Resistance of the Current-Source Load
The current-source load of the CS amplifier in Fig. 1(a) can be implemented using a PMOS transistor biased in the saturation region to provide the required current I, as shown in Fig. 4(a).
Figure 4 (a) The CS amplifier with the current-source load implemented with a p-channel MOSFET Q2; (b) the circuit with Q2 replaced with its large-signal model; and (c) small-signal equivalent circuit of the amplifier.
(a)
(b)
(c)

## Slide 71
We can use the large-signal MOSFET model to model as shown in Fig. 4(b), where
and
Thus the current-source load no longer has an infinite resistance; rather, it has a finite output resistance ro2.
This resistance will in effect appear in parallel with ro1 , as shown in the amplifier equivalent-circuit model in Fig. 4(c), from which we obtain
For instance, if Q2 has an Early voltage equal to that of Q1, ro2 = ro1 and the gain is reduced by half,
(7)
(8)
(9)
(10)

## Slide 72: Contents
The Cascode Amplifier – Cascoding,
The MOS Cascode Amplifier

## Slide 73
The Cascode Amplifier – Cascoding,
Cascoding refers to the use of a transistor connected in the common-gate (or the common-base) configuration to provide current buffering for the output of a common-source (or a common- emitter) amplifying transistor.
Figure 1 illustrates the technique for the MOS case.
In Fig. 1, the transistor CS Q1 is the amplifying transistor and Q2, connected in the CG configuration with a dc bias voltage VG2 (signal ground) at its gate, is the cascode transistor.
The CG amplifier characteristics, we can see that the cascode transistor passes the current gm1vi to the output node.
while multiplying the resistance in its source (ro1of Q1) by a factor K.
The result is the equivalent circuit of Fig. 1, which can be utilized to determine the voltage gain of the cascode amplifier for various load resistances.

## Slide 74
The MOS Cascode Amplifier
Since the load is an ideal constant-current source, the load resistance is infinite.
The amplifier is operating with an open-circuit load, and the gain is
(a)
(b)
Figure 2 (a) A MOS cascode amplifier with an ideal current-source load; (b) equivalent circuit representation of the cascode output.
Now, since Rs of Q2 is ro1, the output resistance Ro is given by the approximate expression
Substituting in Eq. (1) results in
(1)
(2)
For the case gm1 = gm2 = gm and ro1 = ro2 = ro,
(3)
(4)
Thus cascoding increases the gain magnitude from A0 to A20.

## Slide 75
Implementation of the Constant-Current Source Load
Figure 3 (a) A MOS cascode amplifier loaded in a simple PMOS current sourceQ3. (b) Equivalent circuit
at the amplifier output.
(5)
(6)
If the current source load is implemented with a PMOS transistor (which can be part of a PMOS current mirror) as shown in Fig. 3(a), the load resistance RL will be equal to the output resistance of Q3, ro3,
(a)
(b)
and the voltage gain of the cascode amplifier will be
since RL << Ro, the total resistance will be approximately equal to ro3 and the gain will be
(7)
Thus the gain magnitude will be back to A0, of the same order as that realized by a CS amplifier.
A major advantage over the CS circuit: It exhibits a much wider bandwidth.

## Slide 76
The Use of a Cascode Current Source
To realize a gain of the order of A20, the load resistance RL must be of the same order as Ro of the cascode amplifier.
Here Q4 is the current-source transistor, and Q3 is the CG cascode transistor.
This can be achieved by using a cascode current source as shown in Fig. 4.
Figure 4 Employing a cascode transistor Q3 to raise the output resistance of the current source Q4.
Voltages VG3 and VG4 are dc bias voltages.
The cascode transistor Q3 multiplies the output resistance of Q4, ro4 by (gm3ro3) to provide an output resistance for the cascode current source of
(8)

## Slide 77
The Use of a Cascode Current Source
Figure 5 A cascode amplifier with a cascode current-source load.
Combining a cascode amplifier with a cascode current source results in the circuit of Fig. 5(a).
The equivalent circuit at the output side is shown in Fig. 5(b), from which the voltage gain can be easily found as
(9)
(10)
For the case in which all transistors are identical,
(11)

## Slide 78
Distribution of Voltage Gain in a Cascode Amplifier
It is often useful to know how much of the overall voltage gain of a cascode amplifier is realized in each of its two stages: the CS stage Q1, and the CG stage Q2.
In Fig. 6(a), we have included a load resistance RL, which represents the output resistance of the current-source load plus any additional resistance that may be connected to the output node.
Figure 6 (a) The cascode amplifier with a load resistance RL. Only signal quantities are shown. (b) Determining vo1.
(a)
(b)
The voltage gain Av of the amplifier can be found as
(12)
(13)

## Slide 79
Distribution of Voltage Gain in a Cascode Amplifier
The overall gain Av can be expressed as the product of the voltage gains of Q1 and Q2 as
(14)
To obtain Av1 ≡ vo1/vi we need to find the total resistance between the drain of Q1 and ground.
Referring to Fig. 6(b) and denoting this resistance Rd1, we can express Av1 as
Figure 6 (b) Determining vo1.
(b)
From previous expression
we can write
Old expression from previous lecture
Observe that Rd1 is the parallel equivalent of ro1 and Rin2, where Rin2 is the input resistance of the CG transistor Q2.
(15)
Now we can obtain Rd1 as
(16)
(17)

## Slide 80
Distribution of Voltage Gain in a Cascode Amplifier
(18)
and Av1 as
Table 1
Finally, we can obtain Av2 by dividing the total gain Av given by Eq. (13) by Av1.
To provide insight into the effect of the value of RL on the overall gain of the cascode as well as on how this gain is distributed among the two stages of the cascode amplifier.
We provide in Table 1 approximate values for the case ro1= ro2= ro and
(4) for completeness, RL= 0, that is, a signal short circuit at the output.
(3) RL= ro, obtained with a simple current-source load;
(2) RL = (gmro)ro, obtained with a cascode current-source load;
(1) RL =∞, obtained with an ideal current-source load;
For four different values of RL:

## Slide 81: Contents
IC Biasing – Current Sources and Current Mirrors
Problem example

## Slide 82: IC Biasing
Biasing in IC design is based on constant-current sources
  Avoid resistors on IC (issues: chip area, tolerance)
Problem: How to create stable current source
Solution: Current Mirrors (CM)
On IC we may have multiple amplifier stages
  Reference DC current is generated at on CM and is copied at other locations for biasing
  This is known as Current steering
Furthermore, the bias currents of the various stages track each other in case of changes in power-supply voltage or in temperature.

## Slide 83: IC Biasing: Current Source Circuit
For transistor Q1, the drain is shorted to its gate, forcing it to operate in the saturation mode with
Fig. 1 Basic MOSFET Constant Current Source
Since VGS1 = VGS2 = VGS :
Now consider transistor Q2:
(1)
(2)
(3)
The drain current of Q1 is supplied by VDD through resistor R, which in most cases would be outside the IC chip. Since the gate currents are zero,

## Slide 84: IC Biasing: Current Mirror Source Circuit
Fig. 1 Basic MOSFET Constant Current Mirror
Relation between the output current IO to the reference current IREF is determined by geometry of the transistors as follows:
The ration is known as Current Gain or Current Transfer Ration
For identical transistors, Io = IREF and the circuit simply replicates or mirrors the reference current in the output terminal.
Therefore, circuit composed of Q1 and Q2 is called as current mirror
(4)

## Slide 85: IC Biasing: Current Source Circuit
Fig.1 Basic MOSFET Constant Current Source
Fig. 2: Output characteristic (RO) of the current source and current mirror circuits
If considering channel length modulation, IO vary slightly with VO

## Slide 86
Problem Statement 1:
Design the circuit of Figure 1, that is, determine the values of RD and RS – so that the transistor operates at ID = 0.4mA and VD = +0.5V.
The NMOS transistor has Vt = 0.7V, unCox = 100uA/V2, L = 1um, and W = 32um.
Neglect the channel-length modulation effect (i. e. assume that l = 0).
Figure 1

## Slide 87
Solution:
To establish a dc voltage of +0.5 V at the drain, we must select RD as follows:
The saturation-region expression of ID to determine the required value of VOV, since VD = 0.5 V is greater than VG
which results in
we note that the gate is at ground potential. Thus, the source must be at −1.2 V, and the required value of RS can be determined from

## Slide 88
Problem Statement 2:
Design the circuit in Figure 2 to establish a drain voltage of 0.1V.
What is the effective resistance between drain and source at this operating point?
Let Vtn = 1V and k’n(W/L) = 1mA/V2.
Figure 2

## Slide 89
Solution:
Since the drain voltage is lower than the gate voltage by 4.9 V and Vtn =1 V the MOSFET is operating in the triode region. Thus the current ID is given by
The required value for RD can be found as
Since the transistor is operating in the triode region with a small VDS, the effective drain-to-source resistance can be determined as follows:

## Slide 90
Given VDD = 3 V and using IREF =100 μA , design the circuit shown in figure 2 to obtain an output current whose nominal value is 100 μA.
Find R if Q1 and Q2 are matched and have channel lengths of 1 μm , channel widths of 10 μm , Vt = 0.7 V, and kn = 200 μA/V2.
What is the lowest possible value of VO ? Assuming that for this process technology, the Early voltage VA =20 V/μm , find the output resistance of the current source.
Also, find the change in output current resulting from a + 1 V change in VO .
Fig. 2 Current Source circuit
Example: 1

## Slide 91: Solution:
Therefore,
The output current will be 100 μA at VO = VGS = 1 V.
If VO changes by +1 V, the corresponding change in IO will be
Given VDD = 3 V and using IREF =100 μA , design the circuit shown in figure 2 to obtain an output current whose nominal value is 100 μA.
Find R if Q1 and Q2 are matched and have channel lengths of 1 μm , channel widths of 10 μm , Vt = 0.7 V, and kn = 200 μA/V2.
What is the lowest possible value of VO ? Assuming that for this process technology, the Early voltage VA =20 V/μm , find the output resistance of the current source.
Also, find the change in output current resulting from a + 1 V change in VO

## Slide 92
In the current source of Example 1, it is required to reduce the change in output current, ΔIO, corresponding to a change in output voltage, ΔVO, of 1 V to 1% of IO.
What should the dimensions of Q1 and Q2 be changed to?
Assume that Q1 and Q2 are to remain matched.
Example: 2
Fig. 2 Current Source circuit

## Slide 93: Solution: 2
In the current source of Ex. 1, we have IO= 100 µA
To keep VOV of the matched transistors the same as that in Ex. 1, W/L of the transistor should remain the same.
Therefore,
So the dimensions of the matched transistors Q1 and Q2 should be changed to

## Slide 94
For VDD =1.3 V and using IREF=100 μA, it is required to design the circuit of Fig. 3 to obtain an output current whose nominal value is 100 μA.
Find R if Q1 and Q2 are matched with channel lengths of 0.5 μm, channel widths of 5 μm, Vt= 0.4 V, and k’n= 500 μA/V2.
What is the lowest possible value of VO?
Assuming that for this process technology the Early voltage V’A=5 V/μm, find the output resistance of the current source.
Also, find the change in output current resulting from a +0.5 V change in VO.
Example: 3
Fig. 3 Current Source circuit

## Slide 95: Solution: 3
Therefore,
The lowest Vo will be
If VO changes by +0.5 V, the corresponding change in IO will be

## Slide 96
Sketch the p-channel counterpart of the current-source
circuit of Fig. 5. Note that while the circuit of Fig. 5 should more appropriately be called a current sink, the corresponding PMOS circuit is a current source.
Let VDD = 1.3 V, Vt= 0.4 V, Q1 and Q2 be matched, and μpCox = 80 μA/V2.
Find the device W/L ratios and the value of the resistor that sets the value of IREF so that a nominally 80-μA output current is obtained.
The current source is required to operate for VO as high as 1.1 V. Neglect channel-length modulation.
Example: 4
Fig. 5 Current Source circuit

## Slide 97: Solution: 4
Set
Thus

## Slide 98
Consider the current-mirror circuit of Fig. 6 with two transistors having equal channel lengths but with Q2 having a width five times that of Q1.
If IREF is 20 μA and the transistors are operating at an overdrive voltage of 0.2 V, what IO results?
What is the minimum allowable value of VO for proper operation of the current source? If Vt = 0.5 V, at what value of VO will the nominal value of IO be obtained?
If VO increases by 1 V, what is the corresponding increase in IO? Let VA= 20 V.
Example: 5
Fig. 6 Constant Current Mirror

## Slide 99: Solution: 5
If W2 = 5W1 and we let L1 = L2, then we obtain
The corresponding increase in Io, ΔIo is 5 µA
Thus, ID equal 5 IREF will be obtained at

## Slide 100: Contents
Differential Amplifiers: MOS Differential Pair

## Slide 101
Introduction
The differential-pair of differential-amplifier configuration is widely used in IC circuit design.
  One example is input stage of op-amp.
  Another example is emitter-coupled logic (ECL).
Technology was invented in 1940’s for use in vacuum tubes – the basic differential-amplifier configuration was later implemented with discrete bipolar transistors.
However, the configuration became most useful with invention of modern transistor / MOS technologies.

## Slide 102
The MOS Differential Pair
Two matched transistors (Q1 and Q2) joined and biased by a constant current source I.
FET’s should not enter triode region of operation for any type of loading condition.
Figure 1: The basic MOS differential-pair configuration.

## Slide 103
Operation with a Common-Mode Input Voltage
Figure 2: The MOS differential pair with a common-mode input voltage VCM
Consider case when two gate terminals are joined together.
  Connected to a common-mode voltage (VCM).
  vG1 = vG2 = VCM
Since Q1 and Q2 are matched.
Current I will divide equally between the two transistors.
  ID1 = ID2 = I/2, VS = VCM – VGS
    where VGS is the gate-to-source voltage.
(1)

## Slide 104
Operation with a Common-Mode Input Voltage
Figure 2: The MOS differential pair with a common-mode input voltage VCM
Neglecting channel-length modulation, VGS and I/2 are related by
(2)
(3)
(4)
(5)
(6)
Now, let us vary the value of the common-mode voltage VCM.
We see that, as long as Q1 and Q2 remain in the saturation region, the current I will divide equally between Q1 and Q2 and the voltages at the drains will not change.

## Slide 105
Operation with a Differential Input Voltage
If vid is applied to Q1 and Q2 is grounded, following conditions apply:
  vid = vGS1 – vGS2 > 0
  iD1 > iD2
Figure 3: The MOS differential pair with a differential input signal vid applied.
When vid is negative, vGS1 will be lower than vGS2, iD1 will be smaller than iD2, and correspondingly vD1 will be higher than vD2;
In other words, the difference or differential output voltage (vD2 – vD1) will be negative.
The differential pair responds to a difference-mode or differential input signals.

## Slide 106
Operation with a Differential Input Voltage
Figure 3: The MOS differential pair with a differential input signal vid applied.
In the positive direction, when vGS1 reaches the value that corresponds to iD1 = I, and vGS2 is reduced to a value equal to the threshold voltage Vt , at which point vS =−Vt . The value of vGS1 can be found from
where VOV is the overdrive voltage corresponding to a drain current of I/2.
Thus, the value of vid at which the entire bias current I is steered into Q1 is
If vid is increased beyond √2VOV , iD1 remains equal to I, vGS1 remains equal to (Vt+√2VOV ), and vS rises correspondingly, thus keeping Q2 off.

## Slide 107
For the MOS differential pair with a common-mode voltage VCM applied, as shown in Fig. 4, let VDD = VSS = 1.5 V, k’n(W/L) = 4mA/V2, Vt= 0.5 V, I = 0.4 mA, and RD = 2.5 kΩ, and neglect channel-length modulation. Assume that the current source I requires a minimum voltage of 0.4 V to operate properly.
(a) Find VOV and VGS for each transistor.
(b) For VCM = 0, find VS , ID1, ID2, VD1, and VD2.
(c) Repeat (b) for VCM =+1 V.
(d) Repeat (b) for VCM =−0.2 V.
Example: 1
Fig. 4

## Slide 108: Solution 1:
(a) With vG1 = vG2 = VCM, we see that VGS1 = VGS2. Now, since the transistors are matched, I will divide equally between the two transistors,
and
and

## Slide 109: Solution 1:
(b) The analysis for the case VCM = 0 is shown in Fig. 4 (a) from which we see that
and
and
Fig. 4 (a)
VS
VG
VGS
(b) For VCM = 0, find VS , ID1, ID2, VD1, and VD2.

## Slide 110: Solution 1:
(c) The analysis for the case VCM = +1 V is shown in Fig. 4(b) from which we see that
and
and
Fig. 4 (b)
VS
VG
VGS
Observe that the transistors remain in the saturation region as assumed. Also observe that ID1, ID2, VD1, and
VD2 remain unchanged even though the common-mode voltage VCM changed by 1 V.
(c) Repeat (b) for VCM =+1 V.

## Slide 111: Solution 1:
(d) The analysis for the case VCM = − 0.2 V is shown in Fig. 4(c), from which we see that
and
and
So, here again the differential circuit is not responsive to the change in the common-mode voltage VCM.
Fig. 4 (b)
VS
VG
VGS
It follows that the current source I now has a voltage across it of
which is greater than the minimum required value of 0.4 V. Thus, the current source is still operating properly and delivering a constant current I = 0.4 mA and hence
Repeat (b) for VCM =−0.2 V.

## Slide 112: Neil Waste Book

## Slide 113: Static CMOS Design
In order to take advantage of static CMOS, need to learn implementation of AND and OR logic in terms of NAND and NOR gate
Using bubble technique implementation is less complex.
focused on building gates with equal rising and falling delays;
Using smaller pMOS transistors can reduce power, area, and delay.
Compound gates are particularly useful to perform complex functions with relatively low logical efforts.

## Slide 114: Bubble Pushing
AND and OR functions must be built from NAND and NOR gates.
DeMorgan’s law helps with this conversion:
A NAND gate is equivalent to an OR of inverted inputs.
A NOR gate is equivalent to an AND of inverted inputs.
The same relationship applies to gates with more inputs.

## Slide 115
Design a circuit to compute F = AB + CD using NANDs and NORs.

## Slide 117: Logic Effort
In general, the normalized delay of a gate (d) as a process independent unit has two components.
A fixed part called parasitic delay p due to the internal capacitance, when gate driving no load.
Other part proportional to the load on the output called the effort delay or stage effort f
Total delay is measured in units of τ, and is sum of these delays that can be expressed as
d = f + p
f is the effort delay or stage effort that depends on the complexity and fanout of the gate:
f = g×h
Where fanout or electrical effort h.
Where logical effort, g.

## Slide 118: LOGIC EFFORT:
The complexity is represented by the logical effort, g.
Logical effort (g) of a gate is defined as the ratio of the input capacitance (Cin,gate) of the gate to the input capacitance of an inverter (Cin,unit_inv) that can deliver the same output current.
  g = Cin,gate /Cin,unit_inv
  An inverter is defined to have a logical effort of 1. More complex gates have greater logical efforts, indicating that they take longer to drive a given fanout.

## Slide 119: LOGIC EFFORT:
A gate driving h identical copies of itself is said to have a fanout or electrical effort of h.
If the load does not contain identical copies of the gate, the electrical effort can be computed as
where Cout is the capacitance of the external load being driven and Cin is the input capacitance of the gate.
So, the total delay can further expressed as
d = g*h + p
Where, p = Cintinsic,gate/Cintrinsic,inv

## Slide 120: Parasitic Delay
The parasitic delay of a gate is the delay of the gate when it drives zero load.
It can be estimated with RC delay models.
A crude method good for hand calculations is to count only diffusion capacitance on the output node.

## Slide 121: EXAMPLE:
Estimate the logic effort g for the given circuits.

## Slide 125
a circuit with a two way branch.
Consider a path from the primary input to one of the outputs.
The path logical effort G can be expressed as the products of the logical efforts of each stage along the path.
The path logical effort is G= g1x g2= (3/3)x(3/3)=1
The path electrical effort is
H = 90/5 = 18.
Thus, GH = 18.

## Slide 126
The path effort F is the product of the stage efforts of each stage.
F = f1 f2 = (g1h1)(g2h2) = 1 × 6 × 1 × 6 = 36.
F = 2GH
The branching effort b is the ratio of the total capacitance seen by a stage to the capacitance on the path
=(15 + 15)/15 = 2
The path branching effort B is the product of the branching efforts between stages.

## Slide 127: Logic effort for Hi-skew

## Slide 128
Reducing the logical effort on that critical transition to gu = 2.5/3 = 5/6.
The logical effort for the falling transition is estimated by comparing the inverter to a smaller unskewed inverter with equal pulldown current,
a logical effort of gd = 2.5/1.5 = 5/3.
Skewed gates are sometimes denoted with an H or an L on their symbol in a schematic.
Logic effort for Hi-skew

## Slide 129
Logic effort for Lo-skew

## Slide 130: Ratioed Circuit
Ratioed circuits depend on the proper size or resistance of devices for correct operation.
The ratioed gate consists of an nMOS pulldown network and some pullup device called the static load

## Slide 131: P/N Ratios
The average logical effort of the LO-skew NOR2 is actually better than that of the unskewed gate.
In general, what is the best P/N ratio for logic gates (i.e., the ratio of pMOS to nMOS transistor width)?
the ratio giving lowest average delay is the square root of the ratio that gives equal rise and fall delays.
For processes with a mobility ratio of μn/ μp = 2 as we have generally been assuming, the best ratios are shown in Figure

## Slide 132
Reducing the pMOS size from 2 to √2=1.414 for the inverter gives the theoretical fastest average delay, but this delay improvement is only 3%.
However, this significantly reduces the pMOS transistor area.
It also reduces input capacitance, which in turn reduces power consumption.

## Slide 133: Pseudo-nMOS
Neither high-value resistors nor depletion mode transistors are readily available as static loads in most CMOS
Instead, the static load is built from a single pMOS transistor that has its gate grounded so it is always ON.
Larger relative pMOS transistor sizes offer faster rise times but less sharp transfer characteristics.
The pulldown network is like that of an ordinary static gate, but the pullup network has been replaced with a single pMOS transistor that is grounded so it is always ON.

## Slide 134: Pseudo-nMOS
The pMOS transistor widths are selected to be about 1/4 the strength (i.e., 1/2 the effective width) of the nMOS pulldown network as a compromise between noise margin and speed
this best size is process-dependent, but is usually in the range of 1/3 to 1/6.
For example, the logical effort for a falling transition of the pseudo-nMOS inverter is the ratio of its input capacitance (4/3) to that of a unit complementary CMOS inverter (3), i.e., 4/9.
gu is three times as great because the current is 1/3 as much.
The logical effort for each transition is computed as the ratio of the input capacitance to
that of a complementary CMOS inverter with equal current for that transition.

## Slide 135
The parasitic delay is also found by counting output capacitance and comparing it to an inverter with equal current.
For example, the pseudo-nMOS NOR has 10/3 units of diffusion capacitance as compared to 3 for a unit-sized complementary CMOS inverter, so its parasitic delay pulling down is 10/9.
The pullup current is 1/3 as great, so the parasitic delay pulling up is 10/3.
As can be seen, pseudo-nMOS is slower on average than static CMOS for NAND structures.
However, pseudo-nMOS works well for NOR structures.

## Slide 136: Cascode Voltage Switch Logic

## Slide 137: Cascode Voltage Switch Logic

## Slide 138: Cascode Voltage Switch Logic

## Slide 139: Cascode Voltage Switch Logic

## Slide 140: Cascode Voltage Switch Logic

## Slide 141: Cascode Voltage Switch Logic

## Slide 142: Dynamic Circuits
Ratioed circuits reduce the input capacitance by replacing the pMOS transistors connected to the inputs with a single resistive pullup.
The drawbacks of ratioed circuits include slow rising transitions, contention on the falling transitions, static power dissipation, and a nonzero VOL.
Dynamic circuits avoid these drawbacks by using a clocked pullup transistor rather than a pMOS that is always ON.

## Slide 143
Dynamic circuit operation is divided into two modes, as shown in Figure
During precharge, the clock ɸ is 0, so the clocked pMOS is ON and initializes the output Y high.
During evaluation, the clock is 1 and the clocked pMOS turns OFF.
circuits are the fastest commonly used circuit family because they have lower input capacitance and no contention during switching.
They also have zero static power dissipation. However, they require careful clocking, consume significant dynamic power, and are sensitive to noise during evaluation.
The extra transistor is sometimes called a foot.

## Slide 145: Domino Logic
The dynamic-static pair together is called a domino gate
The monotonicity problem can be solved by placing a static CMOS inverter between dynamic gates,
A single clock can be used to precharge and evaluate all the logic gates within the chain.

## Slide 146: Dual-Rail Domino Logic
Dual-rail domino gates accept both true and complementary inputs and compute both true and complementary outputs,

## Slide 147: NP and Zipper Domino
Assignments

## Slide 148: Adders

## Slide 149: Adders
Adder is a digital logic circuit that implements addition of binary numbers.
Adder’s circuit forms a basic component of ALU (Arithmetic Logic Unit).
Adder circuit is basically a combinational logic circuit.
It is a memory less circuit and performs an operation assigned to it
The output depends upon the present input at any given time.

## Slide 150: Classification of Adders
Adders are broadly classified into two types. They are:
Half Adder
Full Adder
Multi-bit Adder
Half Adder
Half Adder is a combinational arithmetic circuit that adds two binary numbers and produces sum bit (S) and carry bit (C) as the output.
It is used to add 2 single-bit binary numbers.

## Slide 151: Full Adder
It is a combinational arithmetic circuit constructed by combining two Half Adder circuits.
It is used to add 3 one-bit binary numbers.
Multi-bit Adder
Multi-bit Adders are constructed using Full Adders either Serially or in Parallel known as:
Serial Adder
Parallel Adder

## Slide 152
FULL ADDER
Block Diagram
Truth Table

## Slide 153: Carry look ahead adder
Carry Look Ahead Adder is an improved version of the ripple carry adder.
It generates the carry-in of each full adder simultaneously without causing any delay.
It is based on the fact that a carry signal will be generated in two cases:
(1) when both bits Ai and Bi are 1, or
(2) when one of the two bits is 1 and the carry-in (carry of the previous stage) is 1.

## Slide 154
The output sum and carry can be defined as
Gi is known as the carry Generate signal since a carry (Ci+1) is generated whenever Gi =1, regardless of the input carry (Ci).
Pi is known as the carry propagate signal, whenever Pi =1, the input carry is propagated to the output carry, i.e., Ci+1. = Ci

## Slide 155: The Boolean expression of the carry outputs of various stages can be written as follows:

## Slide 156: The 4-bit carry look-ahead (CLA) adder consists of 3 levels of logic

## Slide 157
First level: Generates all the P & G signals. Four sets of P & G logic (each consists of an XOR gate and an AND gate). Output signals of this level (P’s & G’s) will be valid after 1τ.
Second level: The Carry Look-Ahead (CLA) logic block which consists of four 2-level implementation logic circuits. It generates the carry signals (C1, C2, C3, and C4) as defined by the above expressions. Output signals of this level (C1, C2, C3, and C4) will be valid after 3τ.
Third level: Four XOR gates which generate the sum signals (Si) (Si = Pi ⊕ Ci). Output signals of this level (S0, S1, S2, and S3) will be valid after 4τ.

## Slide 158: Advantages of Carry Look Ahead Adder
It generates the carry-in for each full adder simultaneously.
It reduces the propagation delay.
Disadvantages of Carry Look Ahead Adder-
It involves complex hardware
It is costlier since it involves complex hardware.
It gets more complicated as the number of bits increases.

## Slide 159: Carry-Save adder
A carry-save adder is a type of digital adder, used to efficiently compute the sum of three or more binary numbers.
It differs from other digital adders in that it outputs two (or more) numbers, and the answer of the original summation can be achieved by adding these outputs together.
A carry save adder is typically used in a binary multiplier, since a binary multiplier involves addition of more than two binary numbers after multiplication.
A big adder implemented using this technique will usually be much faster than conventional addition of those numbers.

## Slide 160: Three bit addition

## Slide 161: Carry save adder

## Slide 162: 7-bit carry save addition

## Slide 163
Clock Skew concept in detail
https://mahajankankit.medium.com/clock-skew-concept-1d5356620895

## Slide 164: Thank you
..