## Slide 1
VLSI DESIGN
Dr. Vijay Rao Kumbhare
Assistant Professor (ECE)
K L University, Hyderabad
22EC2211A and 22EC2211R

## Slide 2: Contents
MOSFET BASICS:-
MODES; MOSFET as switch;
Symbols; VI Characteristics
Previous Lecture
Course introduction with Pre-requisite
Course handout and evaluation pattern
CH, Evaluation Plan, Formative Assessment

## Slide 3: MOSFET Basics
Any voltage-controlled current source can provide signal amplification.
MOSFETs also behave as controlled sources but their characteristics are different from those of bipolar transistors.
A simple geometry consisting of a conductive (e.g., metal) plate, an insulator (“dielectric”), and a doped piece of silicon.
Such a structure operates as a capacitor
Figure 1 (a) Hypothetical semiconductor device, (b) operation as a capacitor, (c) current flow as a result of potential difference.

## Slide 4
Vg < 0
When a negative voltage is applied to the gate
Accumulation
MOSFET Capacitor

## Slide 5
Vg > 0
Depletion
When a small positive voltage is applied to the gate
Depletion
MOSFET Capacitor

## Slide 6
0 > Vg > Vth
Inversion
When a positive voltage above threshold voltage is applied to the gate
Channel
MOSFET Capacitor

## Slide 7: MOSFET
Flow of charge from “Source” to “Drain” is controlled by the “Gate” voltage.
Control by the Gate voltage is achieved by modulating the conductivity of the semiconductor region just below the gate. This region is known as the channel
Metal Oxide Semiconductor Field Effect Transistor
Four terminal device: Source (S), Gate (G), Drain (D), and Body (B).
Fig. 1 Basic Structure of MOSFET

## Slide 8: Mode of Operation
Depletion mode and enhancement mode.
The formation of a channel between the source and drain can act as N-type or P-type MOSFET depending on the carriers doped in the channel region.
Depletion mode: The transistor requires the Gate-Source voltage (VGS) to switch the device “OFF”. The depletion-mode MOSFET is equivalent to a “Normally Closed” switch.
Enhancement Type: The transistor requires a Gate-Source voltage (VGS) to switch the device “ON”. The enhancement-mode MOSFET is equivalent to a “Normally Open” switch.

## Slide 9: N-channel vs. P-channel
For current to flow, VGS > VT
  to form n-type channel at surface
NMOS
PMOS
p-type Si
N+ poly-Si
N+
N+
n-type Si
P+ poly-Si
P+
P+
For current to flow, VGS < VT
  to form p-type channel at surface
Note: VT denotes the threshold voltage, some textbook uses the Vt notation.
Enhancement mode: VT > 0
Enhancement mode: VT < 0
Depletion mode: VT < 0
  Transistor is ON when VG=0V
  Transistor is OFF during - VG
Depletion mode: VT > 0
  Transistor is ON when -VG
  Transistor is OFF during +VG

## Slide 10
Devices | Operating State | Applied Voltage as Gate terminal for | 
 |  | N- channel | P-channel
Depletion type | ON | – VG Turns OFF | +VG Turn OFF
Enhancement type | OFF | + VG Turns ON | – VG Turn ON
Table 1 Types of MOSFET having N-type and P-type channel
Fig. 2 Symbolic representation of n-channel/p-channel MOSFET under (a) depletion condition and (b) enhancement condition.
(a)
(b)

## Slide 11: N-channel Enhancement type MOSFET
Perspective View
Cross-sectional View
Fig. 3 Physical structure of n-channel enhancement MOSFET (a) perspective view and (b) cross-sectional view.

## Slide 12: N-channel Enhancement type MOSFET
The gate electrode is placed on top of a very thin insulating oxide (SiO2) layer.
Fig. 3 Cross-sectional view of n-channel enhancement MOSFET
There are a pair of small n-type regions just under the drain and source electrodes.
If apply a +Ve voltage to gate (G), will push away the “holes” inside the p-type substrate and attracts the moveable electrons in the n-type regions under the source and drain electrodes.
Increasing the +Ve voltage of gate (G) pushes the p-type holes further away and enlarge the thickness of the created channel.
As a result, source to drain current increases-this is why this kind of transistor is called as enhancement mode device.

## Slide 13: P-channel MOSFET
These behave in a similar way, but they pass the current when a –Ve gate voltage creates an effective p-type channel layer under the insulator.
Fig. 4 Cross-sectional view of p-channel enhancement MOSFET
All the voltage and current sign are reversed as compared to N-channel MOSFET.
The free charges that moves from end to end are positively charged (holes).
The PMOS and NMOS transistor are said to be complementary devices.

## Slide 14: Operation of N-channel enhancement MOSFET
For an n-channel device with its source and substrate grounded (i. e., VS=VB=0 V).
For any value of VDS: (Operation with zero gate voltage)
when VGS <0 (accumulation), the source to drain path consists of two back to back diodes.
One of these diodes is always reverse biased regardless of the drain voltage polarity.
when 0<VGS <VT (depletion), there is a deficit of electrons and holes making the channel highly resistive.
No Drain current can flow.
VDS ≥ 0 V
Fig. 5 n-channel enhancement MOSFET at zero gate voltage.

## Slide 15
Consider now the Inversion case:
First, VDS = 0:
when VGS > VT , an induced n- type region, an “inversion layer”, forms in the channel and “electrically connects” the source and drain
The channel is created by inverting the substrate surface from p-type to n type. Hence the induced channel is also called an inversion layer.
The value at which a sufficient number of mobile electrons accumulate in the channel region to form a conducting channel is called the threshold voltage (VT).
VT ranges from 0.3 to 1V.
Fig. 6 n-channel enhancement MOSFET at positive gate voltage.

## Slide 16
Inversion case, VGS > VT (continued): (Applying a small VDS)
When VDS >0 , the induced n-type region allows current to flow between the source and drain.
Fig. 8 Drain current (ID) verses drain voltage (VD) when in the linear or “triode”* region.
Fig. 7 n-channel enhancement MOSFET with VGS>VT and a small VDS applied
The induced channel acts like a simple resistor. Thus, this current, ID, depends linearly on the Drain voltage VD. This mode of operation is called the linear or “triode”* region.

## Slide 17
Inversion case, VGS > VT (continued):
When VDS increases a few tenths of a volt (>0):
Fig. 9 n-channel enhancement MOSFET with VGS>VT and increased VDS .
The depletion region near the drain widens (N+ drain is positively biased – i.e. reverse biased with respect to the substrate).
The electron concentration in the inversion layer near the drain decreases as they are “sucked out” by the drain voltage.
Channel conductance decreases resulting in a drop in the slope of the ID – VD curve.
Fig. 10 Drain current verses drain voltage for increasing VDS (still in the “linear” or triode region).

## Slide 18
Inversion case, VGS > VT (continued):
The inversion layer eventually vanishes near the drain end of the channel. This is called “Pinch-Off” and results in a Flat ID-VDS curve.
The drain-source voltage, VDS, at which this occurs is called the saturation voltage, Vsat while the current is called the saturation current, IDsat.
Fig. 11 The drain current versus the drain-to source voltage for an enhancement type NMOS transistor operated with VGS=VT+VOV.
Where VT and VOV denote threshold voltage and over drive voltage, respectively.

## Slide 19
Inversion case, VGS > VT (continued):
For VDS>Vsat the channel length, L, effectively changes by a value ΔL.
The region of the channel, ΔL is depleted and thus, is high resistivity.
If ΔL ~L, the voltage dropped across the channel (Vsat) varies greatly with VDS due to large modulations in the electric field across the pinched off region ( E=[VDS -Vsat]/[ΔL]).
In this case, ID increases slightly with VDS.
If ΔL <<L, the voltage at the end of the channel will be constant (Vsat ) for all VDS>Vsat.
  ID will be constant.

## Slide 20
Finally,
ID-VDS curves for various VGS:
Fig. 12 The Final drain current versus the drain-to source voltage for an enhancement type NMOS transistor.

## Slide 21: The Depletion type MOSFET
Its structure is similar to that of the enhancement-type MOSFET with one important difference:
The negative VGS is said to deplete the channel of its charge carriers, and this mode of operation (negative VGS) is called depletion mode.
The depletion MOSFET has a physically implanted channel.
An n-channel depletion-type MOSFET has an n-type channel region connecting the n+ source and the n+ drain regions at the top of the p-type substrate.
If a voltage VDS is applied between drain and source, a current ID flows for VGS = 0.
There is no need to induce a channel, unlike the case of the enhancement MOSFET.

## Slide 22: Enhancement Mode verses Depletion Mode MOSFET
N-channel MOSFET
Enhancement mode
Depletion mode
Structure
Symbol

## Slide 23: Derivation of I-V Characteristics
1. Channel Charge Density
From Qch = CV
C is the gate capacitance per unit length and V the voltage difference between the gate and the channel, then Qch is the desired charge density.
C = WCox
V = VGS − VTH because no mobile charge exists for VGS < VTH.
Qch = WCox(VGS − VTH).
Qch is expressed in coulomb/meter.
2. Drain Current at the linear, or triode, region.
Consider a bar of semiconductor having a uniform charge density (per unit length) equal to Qch and carrying a current I

## Slide 24: Derivation of I-V Characteristics
2. Drain Current at the linear, or triode, region. (as long as VDS kept in low level i.e VDS < VGS ‐ VTH)
Drift time, td, is directly proportional to the channel length L, and inversely proportional to the drift velocity of electrons, vd
Drift velocity, vd, is proportional to the horizontal electric field, εy, i.e.:
where µn is the electron mobility in the channel. The value of the horizontal electric field, εy, is, approximately, calculated as follows:
the following expression for IDS can be written as:
where kn is called conductivity factor for NMOS transistors. It is given by:

## Slide 25: Derivation of I-V Characteristics
The NMOS transistor operates in the linear, or triode, region, as long as VDS kept in low level i.e VDS < VGS ‐ VTH
Fig. 1 IDS ‐VDS curves of the NMOS transistor in linear region with VGS as parameter.
IDS is proportional to VDS.
Practically, in linear region, the NMOS transistor acts like a variable resistance, Ron, whose value depends on Vov. Ron is calculated as follows:
2. Drain Current at the linear, or triode, region. (as long as VDS kept in low level i.e VDS < VGS ‐ VTH)
(A)
(B)

## Slide 26: Derivation of I-V Characteristics
3. Drain Current at the linear, or triode, region. (As VDS is increased, the charge channel narrows at the drain end)
VDS modifies the voltage, and, the charge along the channel.
The voltage component due to VDS is maximum at the drain end, while it is zero at the Source end.
Suppose a linear distribution of the voltage component due to VDS along the channel, its average value can be approximately estimated to be VDS/2.
Then, a more accurate calculation of the channel charge can be obtained by adding VDS/2 in the charge expression
A more accurate calculation of the IDS current in linear region is also possible:
Drain Current at the linear, or triode, region.
(C)
(D)

## Slide 27: Derivation of I-V Characteristics
4. Drain Current at Saturation Region (As VDS approaches VGS‐VTH, )
As VDS approaches VGS‐VTH, the channel charge approaches zero at the Drain end.
When VDS compensates for the overdrive voltage VGS‐VTH, VGD results to be equal to the threshold voltage VTH
In this bias condition, no channel charge is available at the Drain end. The conducting channel pinches‐ off, disconnecting the Drain.
The VDS value that produces the channel pinch‐off is called saturation voltage (VDS,sat).
(E)
(F)
Substituting the VDS value in equation A, the expression of the IDS at the pinch‐off is obtained:
For your reference, Eq. A
Therefore, when VDS increases, this depletion region enlarges, and the pinch‐off point moves toward the Source.

## Slide 28: Non-linear effect and Current-voltage characteristics
The characteristics can be measured at dc or at low frequencies and thus are called static characteristics.
where k’n , gDS , and rDS are process transconductance parameter, channel conductance, and linear resistance, respectively.
The dynamic effects that limit the operation of the MOSFET at high frequencies and high switching speeds.

## Slide 29: DC characteristics of MOSFET
Fig. 13 The drain current versus the drain-to source voltage for an enhancement type NMOS transistor.

## Slide 31: Second Order Effects:
Following are the list of second order effects of MOSFET.
Channel length modulation
Velocity Saturation
Mobility Degradation
Threshold voltage – Body effect
Subthreshold region
Drain Punchthrough
Impact Ionization – Hot Electrons

## Slide 32: Channel Length Modulation
Thus, when a high impedance current source is required, longer channel transistors are used.
This reduces the length of the channel which impacts current. The model current equation must be modified to
The length of the channel changes with changing values of VDS.
As the value of VDS is increased, it causes the depletion region of the Drain junction to grow.
In general, lambda is proportional to channel length.
The effects of channel length modulation become more pronounced for smaller feature sizes.

## Slide 33: Channel Length Modulation
This phenomenon yields a larger drain current as VDS increases because ID ∝ 1/L1

## Slide 34: Velocity Saturation
Carrier velocity increases with increasing electric fields.
However, once the critical lateral electric field is reached, the velocity of the carriers does not increase any further.
The current does not increase at the expected rate. Rather, the current increases very little.
At high electric fields (VDS), carrier mobility degrades, eventually leading to a constant velocity.
This is caused by an increased rate of collision and carrier scattering.
Owing to their very short channels (e.g., 0.1 μm), modern MOS devices experience velocity saturation even with drain-source voltages as low as 1 V.
V= μE

## Slide 35: Mobility Degradation
With increasing VGS, vertical electric fields increase.
This increase causes a rise in the number of carrier collisions, which degrades carrier mobility.
The current flowing through the transistor is expected by the ideal models.
Mobility decreases with increasing temperature.

## Slide 36: Body Effect
In MOSFETs, we have assumed that both the source and the substrate (also called the “bulk” or the “body”) are tied to ground.
However, this condition need not hold in all circuits.
An interesting phenomenon occurs as the source-substrate potential difference departs from zero:
The threshold voltage of the device changes.
In particular, as the source becomes more positive with respect to the substrate, VTH increases. Called “body effect,”
If the source terminal rises to a positive voltage while the substrate is at zero, then the source-substrate junction remains reverse-biased and the device still operates properly.

## Slide 37
MOS C-V Characteristics

## Slide 38
MOS C-V Characteristics
There are three types of capacitances are involved that are
capacitance between gate electrode and substrate (Cgb),
capacitance between gate and drain terminals (Cgd) and
capacitance between gate and source terminals (Cgs).

## Slide 39
MOS C-V Characteristics

## Slide 40
MOS C-V Characteristics

## Slide 41
MOS C-V Characteristics
No channel Formation
Under Cutoff region

## Slide 42
MOS C-V Characteristics
Inversion Layer= Channel Formation

## Slide 43
MOS C-V Characteristics
Saturation Region: VDS>Vds-Vth
Channel is in Pinch off condition
More depletion region occur

## Slide 44
MOS C-V Characteristics

## Slide 45: Basic Fabrication Steps

## Slide 46: CMOS Fabrication Process [p-well method]
Assignment: CMOS Fabrication Process [N-well and Twin tube method]

## Slide 70: Metallization Process

## Slide 74: CMOS Fabrication Process [n-well method]

## Slide 75: Fabrication of CMOS
CMOS can be obtained by integrating both the NMOS and PMOS transistors on the same chip substrate.
For integrating NMOS and PMOS devices on the same chip, special regions called as wells are required in which semiconductor type and substrate type are opposite to each other.
A P-well has to be created on a N-substrate or N-well has to be created on a P-substrate.
The fabrication of CMOS is described using the P-substrate, in which the NMOS transistor is fabricated on a P-type substrate and the PMOS transistor is fabricated in N-well.

## Slide 76: Fabrication of CMOS
The fabrication of CMOS can be done by following steps given in the subsequent slides.
Step1: Substrate
Primarily, start the process with a P-substrate.
Step2: Oxidation
The oxidation process is done by using high-purity oxygen and hydrogen, which are exposed in an oxidation furnace approximately at 1000 degree centigrade.
SiO2

## Slide 77: Fabrication of CMOS
Step3: Photoresist
A light-sensitive polymer that softens whenever exposed to light is called as Photoresist layer. It is formed.
Step4: Masking
The photoresist is exposed to UV rays through the N-well mask
SiO2
Photoresist
UV rays
N-well masking
SiO2
Photoresist

## Slide 78: Fabrication of CMOS
Step5: Photoresist removal
A part of the photoresist layer is removed by treating the wafer with the basic or acidic solution.
Step6: Removal of SiO2 using acid etching
The SiO2 oxidation layer is removed through the open area made by the removal of photoresist using hydrofluoric acid.
Photoresist
SiO2
Photoresist
SiO2

## Slide 79: Fabrication of CMOS
Step7: Removal of photoresist
The entire photoresist layer is stripped off, as shown in the below figure.
Step8: Formation of the n-well
By using ion implantation or diffusion process n-well is formed.
SiO2
SiO2

## Slide 80: Fabrication of CMOS
Step9: Removal of SiO2
Using the hydrofluoric acid, the remaining SiO2 is removed.
Step10: Deposition of polysilicon
Polysilicon is deposited on top of a very thin layer of gate oxide using Chemical Vapor Deposition (CVD) process.
Thin gate oxide SiO2
Polysilicon
Thin oxide
Polysilicon

## Slide 81: Fabrication of CMOS
Step11: Removing the layer barring a small area for the Gates
Except the two small regions required for forming the Gates of NMOS and PMOS, the remaining layer is stripped off.
Step12: Oxidation process
Next, an oxidation layer is formed on this layer with two small regions for the formation of the gate terminals of NMOS and PMOS.
Thin gate oxide SiO2
Polysilicon
Thin oxide
Polysilicon

## Slide 82: Fabrication of CMOS
Step13: Masking and N-diffusion
By using the masking process small gaps are made for the purpose of N-diffusion.
The n-type (n+) dopants are diffused or ion implanted, and the three n+ are formed for the formation of the terminals of NMOS.
Thin oxide
Polysilicon

## Slide 83: Fabrication of CMOS
Step14: Oxide stripping
The remaining oxidation layer is stripped off
Step15: P-diffusion
Similar to the above n-diffusion process, the p-diffusion regions are diffused to form the terminals of the PMOS.
Thin oxide
Polysilicon

## Slide 84: Fabrication of CMOS
Step16: Thick field oxide
A thick-field oxide is formed in all regions except the terminals of the PMOS and NMOS.
Step17: Metallization
Aluminum is sputtered on the whole wafer.
Aluminum
Thin oxide
Polysilicon
Aluminum

## Slide 85: Fabrication of CMOS
Step18: Removal of excess metal
The excess metal is removed from the wafer layer.
Step19: Terminals
The terminals of the PMOS and NMOS are made from respective gaps.
Thin oxide
Polysilicon
Aluminum
Contacts

## Slide 86: Fabrication of CMOS
Step20: Assigning the names of the terminals of the NMOS and PMOS
Fabrication of CMOS using P-well process
Among all the fabrication processes of the CMOS, N-well process is mostly used for the fabrication of the CMOS.
P-well process is almost similar to the N-well. But the only difference in p-well process is that it consists of a main N-substrate and, thus, P-wells itself acts as substrate for the N-devices.
B
S
G
D
S
G
D
B
NMOS
PMOS

## Slide 87: Fabrication of BiCMOS
Oxide layer
P-substrate
n+ buried layer
P-Epitaxy
n-well
n-well(collector)
P-base
n+ Emitter
S
G
D
G
D
S
C
B
E
NMOS
PMOS
BJT-NPN
Thick Oxide
n-diffusion
p-diffusion
Thin oxide
Polysilicon

## Slide 88: Stick Diagram

## Slide 89: INTRODUCTION
Objectives:
To know MOS layers
To understand the stick diagrams
To learn design rules
To understand layout and symbolic diagrams
Outcome:
At the end of this, will be able draw the stick diagram, layout and symbolic diagram for simple MOS circuits

## Slide 90: MOS LAYERS
Transistor
Depletion
Transistor
Polysilicon Pin
Diffusion Pin
Metal Pin
Metal-Polysilicon
Metal-Diffusion
Butting
Buried
Polysilicon
Diffusion
Metal
Contact
Implant
Overglass
Buried

## Slide 91: STICK DIAGRAMS
Objectives:
To know what is meant by stick diagram.
To understand the capabilities and limitations of stick diagram.
To learn how to draw stick diagrams for a given MOS circuit.
Outcome:
At the end of this, will be able draw the stick diagram for simple MOS circuits

## Slide 92: STICK DIAGRAMS
VLSI design aims to translate circuit concepts onto silicon.
A popular method of symbolic design ---- stick layout.
Designer draw a free hand sketch of a Layout, using coloured lines to represent various process layers such as Diffusion ( p or n) , Metal and Poly-silicon where
Polysilicon layer crosses diffusion ------- Transistor are created. Metal wires join Diffusion or poly ------- contacts are formed.
Stick diagrams convey layer information through color codes (or monochrome encoding).

## Slide 93: STICK DIAGRAMS
Does show all components/vias.
It shows relative placement of components.
Helps plan the layout and routing
Goes one step closer to the layout
  Via is used to connect higher level metals from metal connection
  Does not show
Transistor sizes
Any other low level details such as parasitics
Wire lengths, wire widths, tub boundaries
  Exact placement of components

## Slide 94: STICK DIAGRAMS
Stick Diagrams – Notations

## Slide 95: NMOS ENCODING
CIF
(Caltech Intermediate Format)
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 96: CMOS ENCODING
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 97: Stick Diagram- Some Rules
Rule 1:
When two or more ‘sticks’ of the same type cross or touch each other that represents electrical contact.
Rule 2:
When two or more “sticks of different type cross or touch each other there is no electrical contact.
(If electrical contact is needed we have to show the connection explicitly)
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 98: Stick Diagram- Some Rules
Rule “3:
When a poly crosses diffusion it represents a transistor.
Note: If a contact is shown then it is not a transistor.
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 99: Stick Diagram- Some Rules
Rule 4:
In CMOS a demarcation line is drawn to avoid touching of p-diff with n-diff.
All PMOS must lie on one side of the line and all NMOS will have to be on the other side.
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 100: Example of Stick Diagram
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 101: Example of Stick Diagram
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 102: nMOS depletion load inverter
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 103: nMOS Enhancement load inverter
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 104: 2 INPUT – CMOS NAND GATE
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 105: 2 INPUT – CMOS NOR GATE
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 106: Examples of Stick Diagrams
NOR gate and NAND using NMOS Transistors
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 107: Examples of Stick Diagrams
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 108: Design Rules
Design rules are communication link b/w the designer specifying requirements and fabricator who materializes them.
First set of Design rules were introduced by Lambda based.
Stick diagram and mask layout is one and the same ,but in mask layout ,aspect ratio (L:W) & distance between any dimensions has to be shown.
Notes: Buried contacts: The buried contact is a method to make direct ohmic contact between the polysilicon gate material and the junctions,

## Slide 128: Design rules define ranges for features
Width: a min. wire widths to avoid breaks
Lambda (λ) is defined as the channel length divided by 2.
λ
Spacing: a min. spacing to avoid shorts
Overlap: a minimum overlaps with the another layers
Most of the industry uses micron rules
Academic uses λ rules to design the layout.
Two types of Design Rules are applicable for industry and academic applications.

## Slide 129: Design Rules
Minimum width of PolySi and diffusion line 2 λ
Minimum width of Metal line 3 λ as metal lines run over a more uneven surface than other conducting layers to ensure their continuity

## Slide 130
PolySi – PolySi space 2λ
Design Rules for spacing
Metal1 – Metal1 space 3λ
Diffusion – Diffusion space 3λ
To avoid the possibility of their associated regions overlapping and conducting current
3λ

## Slide 131
Diffusion – PolySi space λ
Design Rules for spacing
To prevent the lines overlapping to form unwanted capacitor
Metal lines can pass over both diffusion and polySi without electrical effect.
Where no separation is specified, metal lines can overlap or cross

## Slide 132
It is recommended practice to leave λ between a metal edge and a polySi or diffusion line to which it is not electrically connected

## Slide 133: Design Rules

## Slide 134: Recall
– poly-poly spacing 2λ
– diff-diff spacing 3λ
– metal-metal spacing 3λ
– diff-poly spacing λ

## Slide 136
Figure: Stick diagram and corresponding mask layout examples.

## Slide 137
Figure: mask layout examples.

## Slide 138
Figure: mask layout examples.

## Slide 139
Figure: mask layout examples.

## Slide 140: LAYOUTS
Layer Types
– p-substrate
– n-well
– n+
– p+
– Gate oxide
– Gate (polysilicon)
– Field Oxide
Insulated glass
Provide electrical isolation

## Slide 149: Logic Effort
In general, the normalized delay of a gate (d) as a process independent unit has two components.
A fixed part called parasitic delay p due to the internal capacitance, when gate driving no load.
Other part proportional to the load on the output called the effort delay or stage effort f
Total delay is measured in units of τ, and is sum of these delays that can be expressed as
d = f + p
f is the effort delay or stage effort that depends on the complexity and fanout of the gate:
f = g×h
Where fanout or electrical effort h.
Where logical effort, g.

## Slide 150: LOGIC EFFORT:
The complexity is represented by the logical effort, g.
Logical effort (g) of a gate is defined as the ratio of the input capacitance (Cin,gate) of the gate to the input capacitance of an inverter (Cin,unit_inv) that can deliver the same output current.
  g = Cin,gate /Cin,unit_inv
  An inverter is defined to have a logical effort of 1. More complex gates have greater logical efforts, indicating that they take longer to drive a given fanout.

## Slide 151: LOGIC EFFORT:
A gate driving h identical copies of itself is said to have a fanout or electrical effort of h.
If the load does not contain identical copies of the gate, the electrical effort can be computed as
where Cout is the capacitance of the external load being driven and Cin is the input capacitance of the gate.
So, the total delay can further expressed as
d = g*h + p
Where, p = Cintinsic,gate/Cintrinsic,inv

## Slide 152: Parasitic Delay
The parasitic delay of a gate is the delay of the gate when it drives zero load.
It can be estimated with RC delay models.
A crude method good for hand calculations is to count only diffusion capacitance on the output node.

## Slide 153: EXAMPLE:
Estimate the logic effort g for the given circuits.

## Slide 157
a circuit with a two way branch.
Consider a path from the primary input to one of the outputs.
The path logical effort G can be expressed as the products of the logical efforts of each stage along the path.
The path logical effort is G= g1x g2= (3/3)x(3/3)=1
The path electrical effort is
H = 90/5 = 18.
Thus, GH = 18.

## Slide 158
The path effort F is the product of the stage efforts of each stage.
F = f1 f2 = (g1h1)(g2h2) = 1 × 6 × 1 × 6 = 36.
F = 2GH
The branching effort b is the ratio of the total capacitance seen by a stage to the capacitance on the path
=(15 + 15)/15 = 2
The path branching effort B is the product of the branching efforts between stages.

## Slide 159: Logic effort for Hi-skew

## Slide 160
Reducing the logical effort on that critical transition to gu = 2.5/3 = 5/6.
The logical effort for the falling transition is estimated by comparing the inverter to a smaller unskewed inverter with equal pulldown current,
a logical effort of gd = 2.5/1.5 = 5/3.
Skewed gates are sometimes denoted with an H or an L on their symbol in a schematic.
Logic effort for Hi-skew

## Slide 161
Logic effort for Lo-skew

## Slide 162: Inverter with different types of load
Resistive-Load Inverter:
Enhancement-load NMOS Inverter:
Depletion-load NMOS Inverter:

## Slide 163: Different Load Inverter
The input voltage of inverter is equal to the gate to source voltage of nMOS transistor and output voltage of inverter is equal to drain to source voltage of nMOS transistor.
The source to substrate voltage of nMOS is also called driver for transistor which is grounded; so VSS = 0.
The output node is connected with a lumped capacitance used for VTC.

## Slide 164: Resistive Load type Inverter
Here, enhancement type nMOS acts as the driver transistor.
The load consists of a simple linear resistor RL.
The power supply of the circuit is VDD and the drain current ID is equal to the load current IR.
Circuit Operation
When the input of the driver transistor is less than threshold voltage VTH (Vin < VTH), driver transistor is in the cut – off region and does not conduct any current.
Mathematically,
RL
The voltage drop across the load resistor (RL) is ZERO and output voltage is equal to the VDD.
Now, when the input voltage increases further, driver transistor will start conducting the non-zero current and nMOS goes in saturation region.

## Slide 165
VTC of the resistive load inverter, shown below, indicates the operating mode of driver transistor and voltage points.
The chip area occupied by the resistive-load inverter circuit depends on two parameters, the (W/L) ratio of the driver transistor and the value of the resistor RL.
The area of the driver transistor can be approximated by the gate area, (WxL).

## Slide 166: Inverter with N type MOSFET Load
The main advantage of using MOSFET as load device is that the silicon area occupied by the transistor is smaller than the area occupied by the resistive load.
Enhancement Load NMOS
(a) Inverter circuit with saturated enhancement-type nMOS load. (b) Inverter with linear enhancement-type load.
Here, MOSFET is active load and inverter with active load gives a better performance than the inverter with resistive load.
Load transistor can be operated either, in saturation region or in linear region, depending on the bias voltage applied to its gate terminal.

## Slide 167: Inverter with N type MOSFET Load
(a) Inverter circuit with saturated enhancement-type nMOS load. (b) Inverter with linear enhancement-type load.
It requires a single voltage supply and simple fabrication process and so VOH is limited to the VDD − VT. (In Fig. a)
It always operates in linear region; so VOH level is equal to VDD. (In Fig. b)

## Slide 168: Inverter with N type MOSFET Load
Linear load inverter has higher noise margin compared to the saturated enhancement inverter.
The disadvantage of linear enhancement inverter is, it requires two separate power supply and both the circuits suffer from high power dissipation.
Enhancement inverters are not used in any large-scale digital applications.

## Slide 169: Depletion load Inverter
Most of the disadvantages of the enhancement-type load inverter can be avoided by using a depletion-type nMOS transistor as the load device.
The immediate advantages of implementing this circuit configuration are:
sharp VTC transition and better noise margins,
single power supply, and
smaller overall layout area
The fabrication process for producing an inverter with an enhancement-type nMOS driver and a depletion-type nMOS load is slightly more complicated and requires additional processing steps, especially for the channel implant to adjust the threshold voltage of the load device.

## Slide 170: Extra: ALTERMTIVE FORMS OF PULL-UP
4. Complementary transistor pull-up (CMOS):
(a) No current flow either for logical 0 or for logical 1 inputs.
(b) Full logical 1 and 0 levels are presented at the output.
(c) For devices of similar dimensions the p-channel is slower than the n-channel device.

## Slide 171: Inverter Static Characteristics (VTC)
Digital inverter quality is often measured using the Voltage Transfer Curve (VTC), which is a plot of input vs. output voltage.
Ideally, the voltage transfer curve (VTC) appears as an inverted step-function - this would indicate precise switching between on and off - but in real devices, a gradual transition region exists.
The VTC indicates that for low input voltage, the circuit outputs high voltage; for high input, the output tapers off towards 0 volts.
The tolerance to noise can be measured by comparing the minimum input to the maximum output for each region of operation (on / off).
The slope of this transition region is a measure of quality - steep (close to -Infinity) slopes yield precise switching.

## Slide 172: Extra: ALTERMTIVE FORMS OF PULL-UP
Load resistance RL: This arrangement is not often used because of the large space requirements of resistors produced in a silicon substrate.
nMOS depletion mode transistor pull-up:
Dissipation is high ,since rail to rail current flows when Vin = logical 1.
Switching of output from 1 to 0 begins when Vin exceeds Vth of pulldown device.
When switching the output from 1 to 0, the pullup device is non-saturated initially and this presents lower resistance through which to charge capacitive loads .

## Slide 173: Extra: ALTERMTIVE FORMS OF PULL-UP
3. nMOS enhancement mode pull-up .
(a) Dissipation is high since current flows when Vin = logical 1 (VGG is returned to VDD) .
(b) Vout can never reach V DD (logical 1) if V GG = V DD as is normally the case.
(c) VGG may be derived from a switching source, for example, one phase of a clock, so that dissipation can be greatly reduced.
(d) If VGG is higher than VDD then an extra supply rail is required.

## Slide 175: Noise margin

## Slide 176: Noise margin
It is a parameter related to the transfer characteristics.
Similarly, the NH is the difference in magnitude between the minimum HIGH output voltage of the driving gate and the minimum HIGH input voltage recognizable by the driven gate.
NH =|VOH - VIH|
NL is defined as the difference in magnitude between the maximum LOW input voltage recognized by the driven gate and the maximum LOW output voltage of the driving gate.
NL =|VIL - VOL|
It allows one to estimate the allowable noise voltage on the input of a gate so that the output will not be affected.
Noise margin (also called noise immunity) is specified in terms of two parameters - the low noise margin NL, and the high noise margin NH .

## Slide 177: Inverter Dynamic Characteristics
The following are some formal definitions of temporal parameters of digital circuits. All percentages are of the steady state values.
Rise Time (tr) : Time taken to rise from 10% to 90%.
Fall Time (tf): Time taken to fall from 90% to 10%
Edge Rate (trf): (tr + tf )/2.
High-to-Low propagation delay (tpHL): Time taken to fall from VOH to 50%.
Low-to-High propagation delay (tpLH): Time taken to rise from 50% to VOL.
Propagation Delay (tp): (tpHL + tpLH)/2.
Contamination Delay (tcd): Minimum time from the input crossing 50% to the output crossing 50%

## Slide 178: Power Dissipation

## Slide 179: Components of Power Dissipation
Unlike bipolar technologies, here a majority of power dissipation is static, the bulk of power dissipation in properly designed CMOS circuits is the dynamic charging and discharging of capacitances.
There are three main sources of power dissipation:
Thus the total power dissipation, PT, is
Static power dissipation (PS) (due to leakage current when the circuit is idle)
Dynamic power dissipation (PD) (when the circuit is switching)
  Switching or Transient Power Dissipation
  Short circuit power dissipation (PSC)

## Slide 180
CMOS logic is considered to have no static power dissipation.
Static Power Dissipation
Since the ROFF of the two transistors is very large, the DC current driving a capacitive load is zero
This is not completely accurate since MOS transistors have leakage currents associated with the reverse-biased drain-to-substrate connections

## Slide 181
Fig. 1 CMOS inverter model for static power dissipation evaluation
When input = '0', the associated n-device is off and the p-device is on. The output voltage is VDD or logic '1'.
However, there is some small static dissipation due to reverse bias leakage between diffusion regions and the substrate.
Static Power Dissipation
When the input = '1', the associated n-device is on and the p-device turns off. The output voltage is '0' volts or VSS.
It can be seen that one of the transistors is always off when the gate is in either of these logic states.
Since no current flows into the gate terminal, and there is no DC current path from VDD to VSS, the resultant quiescent (steady-state) current, and hence power , Ps is zero.

## Slide 182
Static power consumption is the product of the device leakage current and the supply voltage.
Total static power consumption, PTS, can be obtained as shown in equation 5.
The leakage current Ileakage (current into a device), along with the supply voltage VDD, causes static power consumption in the CMOS devices.
Static Power Dissipation

## Slide 183
Dynamic Power Dissipation
Fig. 3 Power dissipation due to charging/discharging of capacitor
Dynamic power dissipation occurs when the MOS transistor switches to charge and discharge the output load capacitance for a particular node at operating frequency.

## Slide 184
The dynamic dissipation can be modeled by assuming that the rise and fall time of the step input is much less than the repetition period.
Where in= n-device transient current, ip = p-device transient current
For a step input and with
Dynamic Power Dissipation
The average dynamic power, PD, dissipated during switching for a square-wave input, Vin, having a repetition frequency of fp = 1/tp , is given by

## Slide 185
With fp=1/tp, the resulting in
Thus for a repetitive step input the average power that is dissipated is proportional to the energy required to charge and discharge the circuit capacitance.
As can be seen from Eq (10), the power dissipated can be reduced by reducing either the clock frequency, fp , or the load capacitance, CL , or the rail voltage, VDD, or the switching activity parameter.
Dynamic Power Dissipation
The important factor to be noted here is that Eq (10) shows power to be proportional to switching frequency but independent of device parameters.

## Slide 186
Short Circuit Power Dissipation
The short-circuit energy dissipation results due to a direct path current flowing from the power supply to the ground during the switching of a static CMOS gate.
The switching power dissipation is due purely to the energy required to charge and discharge the load capacitance and independent of the rise and fall time of the driving waveform.
Fig. 4 Short Circuit current path
However, in a CMOS circuit if the rise and fall time have finite rise and fall time value, then for a particular time period during switching both nMOS and pMOS transistors will conduct simultaneously.
It provides a direct path between VDD and the ground-rail resulting in short circuit power dissipation.
The current component that passes through both the nMOS and pMOS transistor during switching does not contribute to the charging of the capacitance in the circuit, and hence, it is called short circuit current.

## Slide 187
The short-circuit power dissipation is given by
For the input waveform shown in Fig 5a, which depicts the short-circuit (Fig. 5b) in an unloaded inverter
(a)
(b)
Fig. 5 (a) Input waveform and (b) short circuit current in unloaded inverter
assuming that Vtn = -Vtp and kn=kp and that the behavior is symmetrical around t2.
With Vin(t)= (VDD/tr) tp , t1 =(Vt/VDD)tr and t2=tr/2
Thus for an inverter without load, assuming that tr=tf=(trf)
where tp is the period of the waveform.
Short Circuit Power Dissipation

## Slide 188
Total Power Dissipation
As we saw above, there are three components to the power dissipation of a CMOS inverter:
  Dynamic Power
  Short Circuit Power
  Static Power
Putting them all together, we get the total power consumption, PT, of a CMOS logic gate

## Slide 189
EXAMPLE: Consider 0.1 µm CMOS chip with a clock rate of 100 MHz, VDD = 2V and an average Cload = 3 fF per gate.
(a). What is the dynamic power dissipation per gate?
(b). If the chip incorporates 200,000 gates, what is the power dissipation for the chip? (alpha=0.2)

## Slide 191: Numerical-1
Assume that the Electromigration rule is JAL = 1.0 mA/μm and VDD = 1.8 V.
Find the required power with a 500 MHz clock buffer that drives 5-pF on-chip capacitance.

## Slide 192: Solution-1
The power dissipation of the clock buffer can be obtained using the expression given below

## Slide 193: Numerical-2
As illustrated in Figure 1, suppose that a system with a switching capacitance of 500 pF, operating
at a frequency of 500 MHz, and a supply voltage of 1.8 V can be partitioned into two modules operating at the following conditions.
Module one operates at a frequency of 500 MHz and a supply voltage of 1.8 V. The switching capacitance is 300 pF.
Module two operates at a frequency of 200 MHz and a supply voltage of 1.2 V. The switching capacitance is 200 pF.
Calculate the power saving of the partitioned system.
Figure 1: An example of multiple supply voltages: (a) original system; (b) partitioned system.

## Slide 194: Solution-2
The power dissipation of the original system is
The power dissipation of module one is found to be
The power dissipation of module two is calculated as follows

## Slide 195: Solution-2
As a consequence, the power saving is equal to

## Slide 196: Sources of Power Dissipations
POWER and ENERGY
Power is the instantaneous power in the device, while energy is the integration of power with time.
Figure 1.2 illustrates the difference between power energy.
Fig. 1.2 Power versus Energy
Power is the height of the curve
Lower power could just be slower
Notes: For example, in Fig. 1.2, we can see that approach 1 takes less time but consumes more power than approach 2. But the energy consumed by the two, that is, the area under the curve for both the approaches is the same, and the battery life is primarily determined by this energy consumed.

## Slide 197: Sources of Power Dissipations
Power dissipation is measured commonly in terms of two types of metrics:
Peak power: Peak power consumed by a particular device is the highest amount of power it can consume at any time.
The high value of peak power is generally related to failures like melting of some interconnections and power-line glitches.
Average power: Average power consumed by a device is the mean of the amount of power it consumes over a time period.
High values of average power lead to problems in packaging and cooling of VLSI chips.

## Slide 198: Type of Power

## Slide 199: Type of Power
Dynamic power is the power consumed when the device is active, that is, when the signals of the design changing its value.
Static power is the power consumed when the device is powered up but no signals are changing value.
In CMOS devices, the static power consumption is due to leakage mechanism.
Dynamic Power Dissipation
Static Power Dissipation
It is generally categorized into three types:
Switching Power
Short-Circuit Power
Glitching Power

## Slide 200: Dynamic Power Dissipation
The first and primary source of dynamic power consumption is the Switching power dissipation occurs due the power required to charging and discharging of the output capacitance on a gate.
(1) Switching Power Dissipation
Fig. 1.4 Dynamic (switching) power.
The energy per transition is given by
𝑬𝒏𝒆𝒓𝒈𝒚 Per 𝑻𝒓𝒂𝒏𝒔𝒊𝒕𝒊𝒐𝒏= 𝑪𝑳 × 𝑽2𝒅𝒅
Where CL is the load capacitance and Vdd is the supply voltage
Switching power is therefore expressed as:
𝑷𝒔𝒘𝒊𝒕𝒄𝒉 = (𝑬𝒏𝒆𝒓𝒈𝒚/ 𝑻𝒓𝒂𝒏𝒔𝒊𝒕𝒊𝒐𝒏) × 𝒇
= 𝑪𝑳 × 𝑽2𝒅𝒅 × 𝑷𝒕𝒓𝒂𝒏𝒔 × 𝒇𝒄𝒍𝒐𝒄𝒌
Where f is the frequency of transitions, Ptrans is the probability of an output transition and fclock is the frequency of the system clock
Notes: In addition to the switching power dissipation for charging and discharging the load capacitance, switching power dissipation also occurs for charging and discharging of the internal node capacitance. Thus, total switching power dissipation is given by
𝐏𝐭𝐨𝐭𝐚𝐥𝐬𝐰𝐢𝐭𝐜𝐡 = 𝐂𝐋 × 𝐕𝐝𝐝 𝟐 × 𝐏𝐭𝐫𝐚𝐧𝐬 × 𝐟𝐜𝐥𝐨𝐜𝐤 + ∑ 𝛂𝐢 × 𝐂𝐢 × 𝐕𝐝𝐝 × (𝐕𝐝𝐝 − 𝐕𝐭𝐡) × 𝐟𝐜𝐥𝐨𝐜𝐤 (1.3)
Where αi and Ci are the transition probability and capacitance, respectively, for an internal node i.

## Slide 201: Dynamic Power Dissipation
Switching Power Dissipation
Fig. 1.4 Dynamic (switching) power.
Low-to-High Transition Equivalent Circuit
Energy Drawn From Power Supply

## Slide 202: Dynamic Power Dissipation
Switching Power Dissipation
Fig. 1.4 Dynamic (switching) power.
Low-to-High Transition Equivalent Circuit
Energy Stored on Load Capacitor
Compared to EVDD, we see that CLV2/2 dissipated
Same amount dissipated when capacitor discharged
Independent of MOSFET resistance

## Slide 203: Dynamic Power Dissipation
(2) Short-Circuit Power Dissipation
In addition to the switching power, short-circuit power also contributes to the dynamic power.
Short-circuit currents occur when both the negative metal–oxide–semiconductor (NMOS) and positive metal–oxide–semiconductor (PMOS) transistors are ON
Let Vtn be the threshold voltage of the NMOS transistor and Vtp is the threshold voltage of the PMOS transistor.
Fig. 1.5 Short-circuit current or crowbar current.
Then, in the period when the voltage value is between Vtn and Vdd–Vtp, while the input is switching either from 1 to 0 or vice versa, both the PMOS and the NMOS transistors remain ON, and the short-circuit current follows from Vdd to ground (GND).

## Slide 204: Dynamic Power Dissipation
Fig. 1.5 Short-circuit current or crowbar current.
The expression for short-circuit power is given by
Where tsc is the rise/fall time duration of the short-circuit current
Ipeak is the total internal switching current (short-circuit current plus the current to charge the internal capacitance)
μ is the mobility of the charge carrier
εox is the permittivity of the silicon dioxide
W is the width
L is the length
D is the thickness of the silicon dioxide.
Notes: From the above equation it is evident that the short-circuit power dissipation depends on the supply voltage, rise/fall time of the input and the clock frequency apart from the physical parameters. So the short-circuit power can be kept low if the ramp (rise/fall) time of the input signal is short for each transition. Then the overall dynamic power is determined by the switching power.

## Slide 205: Dynamic Power Dissipation
(2) Short-Circuit Power Dissipation (Detailed Derivation)
Fig. 1.5 Short-circuit current or crowbar current.
When there are finite rise and fall times at the input of CMOS logic gates, both pMOS and nMOS transistors are simultaneously ON for a certain duration, shorting the power supply line to ground.
This leads to current flow from supply to ground.

## Slide 206: Dynamic Power Dissipation
The third type of dynamic power dissipation is the glitching power which arises due to finite delay of the gates.
(3) Glitching Power Dissipation
Glitches often occur when paths with unequal propagation delays converge at the same point in the circuit.
Glitches occur because the input signals to a particular logic block arrive at different times, causing a number of intermediate transitions to occur before the output of the logic block stabilizes.
These additional transitions result in power dissipation, which is categorized as the glitching power.
Glitches are temporary changes in the value of the output – unnecessary transitions

## Slide 207
Impact of Technology Scaling

## Slide 208: Technology Evolution
Today’s complex VLSI chips
  The number of transistors has exceeded 120 million
  Die area is typically about 1cm2
Moore’s low (Gordon Moore, one of the cofounders of the Intel Corporation)
  The number of transistors on a chip would double about every 18 months
Design team and design hierarchy are needed to realize a complex chip

## Slide 209
Why more transistors per IC?
  Smaller transistors
  Larger dice
Why faster computers?
  Smaller, faster transistors
  Better microarchitecture
  Fewer gate delays per cycle

## Slide 210: MOS Scaling
Reduction is symmetric and preserves geometric ratios which are important to the functioning of the chip. Ideally, allows design reuse.
Assume that S is the scaling factor. Then a transistor with original dimensions of L and W becomes a transistor with dimensions L/S and W/S.
Reduction in size of an MOS chip by reducing the dimensions of MOSFETs and interconnects.

## Slide 211
W ‘=W/S
Drain
Fig. 1 Scaling of device by factor of S
Two major forms of scaling
Full scaling (constant-field scaling) – All dimensions are scaled by S and the supply voltage and other voltages are so scaled.
Constant-voltage scaling – The voltages are not scaled and, in some cases, dimensions associated with voltage are not scaled.

## Slide 212: Constant Field Scaling
Proposed by Dennard in 1974
Also known as constant field scaling or Full scaling.
  Voltage and MOSFET dimensions are scaled by the same factor S>1, so that the electric fields remains unchanged.

## Slide 213: Constant Voltage Scaling
More preferred
All dimensions are scaled down except power supply and terminal voltages.
Increase in drain current density and power density by a factor of S3 adversely effecting device reliability.
That causes problems like
  Electromigration
  Hot Carrier Degradation
  Gate Oxide Breakdown
  Electrical Over-stress

## Slide 214
Quantity | Sensitivity | Constant Field | Constant Voltage
Scaling Parameters |  |  | 
Length | L | 1/S | 1/S
Width | W | 1/S | 1/S
Gate Oxide Thickness | tox | 1/S | 1/S
Supply Voltage | Vdd | 1/S | 1
Threshold Voltage | VT0 | 1/S | 1
Doping Density | NA, ND | S | S2
Device Characteristics |  |  | 
Area (A) | WL | 1/S2 | 1/S2
 | W/Ltox | S | S
D-S Current (IDS) | (Vdd - vT)2 | 1/S | S
Gate Capacitance (Cg) | WL/tox | 1/S | 1/S
Transistor On-Resistance (Rtr) | Vdd/IDS | 1 | 1/S
Intrinsic Gate Delay () | RtrCg | 1/S | 1/S2
Clock Frequency | f=1/ | S | S2
Power Dissipation (P) | IDSVdd | 1/S2 | S
Power Dissipation Density (P/A) | P/A | 1 | S3

## Slide 215: Observations of scaling
Constant field scaling:
Gate capacitance per micron is nearly independent of process
Gates get faster by a factor of S.
Dynamic power goes down with scaling.
Constant voltage scaling:
Gates get faster by a factor of S2.
Power density increased by a factor of S3.
Current density goes up with scaling.

## Slide 216: Thank you
..
Dr. Shyama Prasad Mukherjee International Institute of Information Technology, Naya Raipur

## Slide 217: Impact of Constant-Field Scaling
(1)
(2)
(3)

## Slide 218: Impact of Constant-Field Scaling
(4)
(5)
(6)

## Slide 219: Impact of Constant-Voltage Scaling
(a) Scaling of gate oxide capacitance per unit area:
Here, the gate capacitance per unit area is increased by a factor of S.
(b) Scaling of transconductance:
Here, the transconductance is increased by a factor of S.
(c) Scaling of linear mode drain current:
Here, the linear mode drain current is increased by a factor of S.
(7)
(8)
(9)

## Slide 220: Impact of Constant-Voltage Scaling
(d) Scaling of Saturation mode drain current:
Here, the saturation mode drain current is increased by a factor of S.
(e) Scaling of power dissipation and power density:
and
Here, the power dissipation and power density are increased by a factor of S and S3, respectively.
(10)
(11)

## Slide 221: Thank you
..